## Slide 1: Mathematical Modeling
Prof. Ing. Michele MICCIO
Dept. of Industrial Engineering (Università di Salerno)
Prodal Scarl (Fisciano)
Rev. 7.01 of December 10, 2014
Notes: 1

## Slide 2: TYPES OF MODELS
Models are used not only in the natural sciences (such as physics, biology, life sciences, earth science, meteorology) and engineering-architecture disciplines, but also in the social sciences (such as economics, psychology, sociology and political science).
Here is a list:
· Physical Models
· Analogic Models
· Provisional Theories (e.g., molecular and atomic models)
· Maps and Drawings (e.g., PI&D, geographycal maps, etc.)
· Mathematical and symbolic models
 § 1.4 in Himmelblau D.M. e Bischoff K.B., “Process Analysis and Simulation”, Wiley & Sons Inc., 1967

## Slide 3: Why modeling? Some answers …
Models are usually more accessible to study than the actual system modeled.
Changes in the structure of a model are easier to implement, and changes in the behavior of a model are easier to isolate, understand, and communicate to others.
A model can be used to achieve insight when direct observation/experimentation with the actual system is too dangerous, disruptive, or demanding.
A model can be used to answer questions about a system that has not yet been observed or built, or even one that cannot be observed or built with present technologies.

## Slide 4: MATHEMATICAL MODELING
A mathematical model is a description of a system using mathematical concepts and language.
The process of developing a mathematical model is termed mathematical modeling.
Mathematical models are used not only in the NATURAL SCIENCES (such as physics, biology, earth science, meteorology) and ENGINEERING DISCIPLINES (e.g. computer science, artificial intelligence), but also in the SOCIAL SCIENCES (such as economics, psychology, sociology and political science);
physicists, engineers, statisticians, operations research analysts and economists use mathematical models most extensively.
A model may help to explain a system and to study the effects of different components, and to make predictions about behavior.

## Slide 5: MATHEMATICAL MODELING
General statements
A mathematical model usually describes a system by a set of variables and a set of equations that establish relationships between the variables.
Relationships can be described by operators, such as algebraic operators, functions, differential operators, etc.
Anonymous
A mathematical model is a representation, in mathematical terms, of certain aspects of a non-mathematical system
Aris, 1999
A model may be prescriptive or illustrative, but, above all, it must be useful !
Wilson, 1991

## Slide 6: Why Math Modeling ?
Is it:
  to design a controller?
  to analyze the performance of the process?
  to understand the process/system better?
  to simplify the complexity of a system?
Introduction to Process Control Romagnoli & Palazoglu

## Slide 7: Mathematical model development strategy
The development of a model and its structure are intimately related to the goals of modeling.
In other words, the complexity of a model should be commensurate with the ultimate application in which it will be used.
In model development, always start by trying the simplest model and then only add complexity to the extent needed
Introduction to Process Control Romagnoli & Palazoglu
Keep things as simple as possible, but not simpler
A. Einstein

## Slide 8: Mathematical model development: Complexity vs. Simplicity
Introduction to Process Control Romagnoli & Palazoglu
Ratio of costs to benefits

## Slide 9: Mathematical model development strategy: cycling

## Slide 10: Mathematical model development strategy: cycling (2)
Problem description
Mathematical representation
Parameter tuning
Validation
ko
Data collection
ko
Model use
ok
From
Prof. Giorgio Guariso slides

## Slide 11: Validation
In modeling and simulation, the process of determining the degree to which a model or simulation is an accurate representation of the real world from the perspective of the intended uses of the model or simulation.
From 
http://www.thefreedictionary.com

## Slide 12: VARIABLES Definition
A variable represents a relevant property of the system, being modeled.
A variable can be, for example, physical or chemical quantities, measured system outputs often in the form of signals, timing data, counters, and event occurrence (yes/no).
Mathematically, a variable can be an unknown appearing in equations and disequations or a function of one or more independent variables.
 The actual model is the set of functions that describe the relations between the different variables.
Notes: NEW

## Slide 13: VARIABLES Examples
The most common variables in chemical and process engineering are:
1. composition/concentration
2. temperature
3. pressure
4. rate
5. repetition variable
Variables 1 to 3 are referred to as “intensive” as they do not depend on mass or size of the system being considered.
A rate can be related to matter (mass, mole, volume) or energy (heat) or momentum (force).
Rate is an “extensive” variable.
A repetition variable is used to account for realization of a given operation through a number of stages or units, being all equal in their working principle.
Generally, each variable is defined in a given interval.
NV = No. of variables in the model being considered.

## Slide 14: COMPOSITION VARIABLES
Notes: NEW

## Slide 15: VARIABLES 1st Classification (on the base of the mathematical set membership)
A variable can be, depending on its value:
  real
  natural
  integer
  boolean
  strings
 A variable can be “continuous” or “discrete”.
Notes: NEW

## Slide 16: VARIABLES 2nd Classification (on the base of the role in engineering calculations)
Specified variables or Specifications
They are those variables that represent physical-chemical properties or that are fixed by designers, regulations, environmental considerations, etc. prior to the design phase.
Design variables
They are variables selected by designers.
Generally, their values are chosen in order to satisfy an optimum condition for a given “objective function”.
Unknown variables
They are those variables that are calculated by the available system of equations once values for Design Variables have been fixed.

## Slide 17: Mathematical Models 1st classification
  “First principles Models”
    Basic models
    Models involving transport phenomena
    Models based on the “population balance approach”
  Empirical or “fitting” models
  Dynamic models
    dynamic models with “input-output representation”
    state-space dynamic models
    black box dynamic models
  Time Series
  Statistical models
(on the base of the approach adopted for model development)
Deterministic Models
 rielaborated from § 1.4 in Himmelblau D.M. e Bischoff K.B., “Process Analysis and Simulation”, Wiley & Sons Inc., 1967
Notes: new

## Slide 18: Mathematical Models 1st classification
  First principles Models
  or Fundamental Models ( Palazoglu & Romagnoli, 2005) or Mechanistic or White Box Models ( Roffel & Betlem, 2006)
    Modelli basati sui “fenomeni di trasporto”
  Modelli basati sul “bilancio di popolazione”
  Modelli empirici o di “fitting”
  Modelli dinamici
    Modelli dinamici “con rappresentazione ingresso-uscita”
    Modelli dinamici “con rappresentazione nello spazio di stato”
    Modelli dinamici a scatola nera (black box)
  Serie temporali
  Modelli statistici
(on the base of the approach adopted for model development)

## Slide 19: FUNDAMENTAL LAW
GENERAL CONSERVATION PRINCIPLE
[IN] – [OUT] + [GEN] = [ACC]
NB: GEN > 0  formation
GEN < 0  disappearance
SIMPLER CASES
For a chemical element:
IN - OUT = ACC
At steady-state:
IN - OUT + GEN = 0
At steady-state and without chemical/biochemical reactions:
IN - OUT = 0
Notes: new

## Slide 20: First principles models (including population balance models)
NB:
The description of such a system and the development of such a model require the concept of:
control volume
or
system boundary

## Slide 21: Mathematical Models 1st classification
  “First principles Models”
    Basic models
    Models involving transport phenomena
    Models based on the “population balance approach”
  Empirical or “fitting” models
  Dynamic models
    dynamic models with “input-output representation”
    state-space dynamic models
    black box dynamic models
  Time Series
  Statistical models
(on the base of the approach adopted for model development)
 rielaborated from § 1.4 in Himmelblau D.M. e Bischoff K.B., “Process Analysis and Simulation”, Wiley & Sons Inc., 1967
Notes: NEW

## Slide 22: First principles mathematical models. Malthusian Growth Model
An Early and Very Famous Population Model
In 1798 the Englishman Thomas R. Malthus posited a mathematical model of population growth. He model, though simple, has become a basis for most future modeling of biological populations. His essay, "An Essay on the Principle of Population," contains an excellent discussion of the caveats of mathematical modeling and should be required reading for all serious students of the discipline. Malthus's observation was that, unchecked by environmental or social constraints, it appeared that human populations doubled every twenty-five years, regardless of the initial population size. Said another way, he posited that populations increased by a fixed proportion over a given period of time and that, absent constraints, this proportion was not affected by the size of the population.
By way of example, according to Malthus, if a population of 100 individuals increased to a population 135 individuals over the course of, say, five years, then a population of 1000 individuals would increase to 1350 individuals over the same period of time.
Malthus's model is an example of a model with one variable and one parameter. A variable is the quantity we are interested in observing. They usually change over time. Parameters are quantities which are known to the modeler before the model is constructed. Often they are constants, although it is possible for a parameter to change over time. In the Malthusian model the variable is the population and the parameter is the population growth rate.

## Slide 23: Example No. 1 Malthusian Growth Model
PARAMETERS
STATE VARIABLES
CLASSIFICATION
DYNAMIC AUTONOMOUS MATHEMATICAL MODEL
made by 1 ODE (Order =1) ,
LINEAR, CONSTANT COEFFICIENT MODEL
GENERAL CONSERVATION LAW applied to No. of individuals in a “closed system”: ACC = GEN
GEN = birth - death
INITIAL CONDITION:

## Slide 24: Example No. 2 Logistic Model
Differently from the Malthusian model …
developed by Belgian mathematician Pierre Verhulst (1838)
HYPOTHESES
resources are limited for growth: N(t)≤Nsat
GENERAL CONSERVATION LAW applied to No. of individuals in a “closed system”: ACC = GEN GEN = birth - death
PARAMETERS
STATE VARIABLES
CLASSIFICATION
Dynamic autonomous mathematical model
made by 1 ODE (Order =1) ,
non linear, constant coefficient model
Notes: NEW

## Slide 25: First principles mathematical models. The prey-predator model
BIBLIO REF.
Lotka A.J. (1925) Elements of Physical Biology. Baltimore: Williams & Wilkens.
Volterra V. (1926) "Variazioni e fluttuazioni del numero d’individui in specie animali conviventi", Mem.R.Accad.Naz.dei Lincei, Ser.VI, 2 1st president of National Research Council (CNR) of Italy
The idea is that, if left to themselves with an infinite food supply, the rabbits or zebras would live happily and experience exponential population growth.
On the other hand, if the foxes or lions were left with no prey to eat, they would die faster than they could reproduce, and would experience exponential population decline.

## Slide 26: First principles mathematical models. The prey-predator model
ASSUMPTIONS
In words, the model states that:
Each prey gives rise to a constant number of offspring per year; In other words, there are no other factors limiting prey population growth apart from predation.
Each predator eats a constant proportion of the prey population per year; In other words, doubling the prey population will double the number eaten per predator, regardless of how big the prey population is.
Predator reproduction is directly proportional to prey consumed; Another way of expressing this is that a certain number of prey consumed results in one new predator; or that one prey consumed produces some fraction of a new predator.
A constant proportion of the predator population dies per year. In other words, the predator death rate is independent of the amount of food available.

## Slide 27: Example No. 3 The prey-predator model
VECTOR OF
PARAMETERS
STATE VARIABLE
VECTOR
INITIAL CONDITION
interaction term
“maltusian” term
CLASSIFICATION
DYNAMIC AUTONOMOUS MATHEMATICAL MODEL
made by 2 ODEs (Order = 2) ,
NON LINEAR, CONSTANT COEFFICIENT MODEL
GENERAL CONSERVATION LAW applied to No. of individuals in a “closed system”: ACC = GEN
GEN = birth - death

## Slide 28: First principles mathematical models. The prey-predator model with 2 parameters
INITIAL CONDITION
STEADY-STATE or EQUILIBRIUM POINTS
carrying capacity
 Cleve Moler, Experiments with MATLAB, 2009
http://www.mathworks.com/moler/exm/chapters.html
Notes: 28

## Slide 29: First principles mathematical models. The prey-predator model Issues related to mathematical solution
TYPES OF SOLUTION
  Steady-state solutions
  Periodic solutions
STABILITY OF SOLUTIONS
http://www.scholarpedia.org/article/Predator-prey_model
Time profile
or
Time series

## Slide 30: First principles mathematical models. The prey-predator model with 2 parameters
MatLab SOLUTION (1)
function yp = lotka(t,y)
%LOTKA Lotka-Volterra predator-prey model.
% Copyright 1984-2002 The MathWorks, Inc.
% Revision: 5.9 by Michele MICCIO: May 8, 2008
% suggested parameters in the original file by MatLab:
% ALPHA=0.01
% BETA=0.02
yp = diag([1 - ALPHA*y(2), -1 + BETA*y(1)])*y;
run file LOTKADEMO.M
calling function LOTKA.M
Notes: 30

## Slide 31: First principles mathematical models. The prey-predator model with 2 parameters
MatLab SOLUTION (2)
function predprey(action)
% PREDPREY Predator-prey GUI.
% Drag the red dot to change equilibrium point.
% Drag the blue-green dot to change the initial conditions.
% Default parameters.
mu = [300 200]'; % Equilibrium.
eta = [400 100]'; % Initial conditions.
% Predator-prey ode
function ydot = ppode(t,y);
ydot = [(1-y(2)/mu(2))*y(1);
-(1-y(1)/mu(1))*y(2)];
end
run file PREDPREY.M
Use of graphycal interface
Notes: 31
31

## Slide 32: First principles mathematical models. The prey-predator model with 2 parameters
predprey.m
Phase portrait
Time profile
or
Time series
Notes: 32

## Slide 33: Mathematical Models 1st classification
  “First principles Models”
    Basic models
    Models involving transport phenomena
    Models based on the “population balance approach”
  Empirical or “fitting” models
  Dynamic models
    dynamic models with “input-output representation”
    state-space dynamic models
    black box dynamic models
  Time Series
  Statistical models
(on the base of the approach adopted for model development)
 rielaborated from § 1.4 in Himmelblau D.M. e Bischoff K.B., “Process Analysis and Simulation”, Wiley & Sons Inc., 1967
Notes: NEW

## Slide 34: Transport Phenomena
Examples:
Newton law of viscosity
Fourier law of heat conduction
1st Fick law of diffusion
General Law

## Slide 35: Transport and Kinetic Rate Equations
Momentum, Heat and Mass transfers
 | Heat | Mass | Momentum
Flux | q | nA | τxy
Diffusion transfer (microscopic scale) |  |  | 
Law | Fourier’s law | Fick’s law | Newton’s law
Driving force (gradient) | dT/dx | dCA/dx | dvy/dx
Key parameter (diffusion coefficient) | kT (Thermal conductivity) | DAB (Diffusivity) | µ (Viscosity)
Convection transfer (macroscopic scale) |  |  | 
Driving force | ∆T | ∆CA | ∆P

## Slide 36: Mathematical Models 1st classification
  “First principle Models”
    Basic models
    Models involving trasport phenomena
    Models based on the “population balance approach”
  Empirical or “fitting” models
  Dynamic models
    dynamic models with “input-output rappresentation”
    state-space dynamic models
    black box dynamic models
  Time Series
  Statistical models
(on the base of the approach adopted for model development)
 rielaborated from § 1.4 in Himmelblau D.M. e Bischoff K.B., “Process Analysis and Simulation”, Wiley & Sons Inc., 1967
Notes: NEW

## Slide 37: Mathematical Models 1st classification
  “First principle Models”
    Basic models
    Models involving trasport phenomena
    Models based on the “population balance approach”
  Empirical or “fitting” models
  Dynamic models
    input-output dynamic models
    input-state-output dynamic models or state-space models
    dynamic black box models
  Time Series
  Statistical models
(on the base of the approach adopted for model development)
 rielaborated from § 1.4 in Himmelblau D.M. e Bischoff K.B., “Process Analysis and Simulation”, Wiley & Sons Inc., 1967

## Slide 38: Mathematical Models 2nd classification
Structured or Theoretical or White Box Models
Unstructured or Empirical or Black Box Models
Hybrid or Gray Box Models
(on the base of an approach typical of process engineering)
 Ogunnaike B.A. and Ray W.H., “Process Dynamics, Modeling and Control”, Oxford Univ. Press, 1994
 Romagnoli & Palazoglu, "Introduction to Process Control"

## Slide 39: Structured models
Characteristics:
Using mathematical equations describe the system
a) Conservation equations e.g. total mass, mass of individual chemical species, total energy, momentum and number of particles.
b) Rate equations e.g. transport rate and reaction rate equation.
c) Equilibrium equation e.g. reaction and phase equilibrium.
Equations of state e.g. ideal gas law
Other constitutive relationships e.g. Control valve flow equation, PID control law
 Advantages:
Being able of understanding the process in a fundamental way from this modeling
 Disadvantages:
It requires a good and reliable understanding of the physical and chemical phenomena that underlie the process
Accuracy of model depends on the assumptions and mathematical ability of the person constructing the model.

## Slide 40: Unstructured models
Characteristic: constructing (fitting) a mathematical relationship among the variables that can explain the observed data.
a) Vary input variables and then measure the response of the output variables.
b) Enough experiments are required (a historical database of measurements or observations is needed)
c) Such models that rely solely on empirical information are considered as black-box models.
Example: A black-box model simulating the internal combustion engine operation and implemented into the control box of a modern car
 Advantages:
a) Good indicator to actual process (no assumption required).
b) Just focus in on the range of conditions under the operating process.
 Disadvantages:
a) It requires an actual operating process and may become very time-consuming and costly
b) It doesn’t allow extrapolation, generally
c) It never gives the engineer a fundamental understanding of the process.
black box
Model
i
y

## Slide 41: Structured and unStructured Models: Comparison
Structured Models theory-rich and data-poor
Unstructured Models data-rich and theory-poor

## Slide 42: “Hybrid” Models
Empirical Model II (Gray-Box) is developed by incorporating empirical knowledge into the fundamental understanding of the process.
Such models blending fundamental and empirical knowledge are referred to as gray-box models.
  Example
  An example can be the use of mass and energy balances to develop a reactor model and the rate of the reaction will be based on expressions obtained from laboratory experiments.
Introduction to Process Control Romagnoli & Palazoglu

## Slide 43: Mathematical Models 3rd classification
 Ch.3 of Himmelblau D.M. and Bischoff K.B., “Process Analysis and Simulation”, Wiley, 1967
on the base of
mathematical features of equations and variables,
also affecting type or easiness of solution
deterministic vs stocastic
lumped parameters vs distributed parameters
one dimension vs several dimensions
linear vs non linear
steady state vs time dependent
time-invariant vs time – varying
autonomous vs non – autonomous
  Dynamical models

## Slide 44: Example No. 4 Modeling of salami drying
1st approach
lumped parameters
r [mm]
X [ kg (H2O/ kg (S.S.) ]
2nd approach
distributed parameters
Description of internal moisture profile
X [=] mass of H2O (liq.) / mass of dry solids
r [mm]
Notes: ---> presentation_MMPIA_2014-15.ppt

## Slide 45: Modeling of salami drying: Other assumptions
Sausage is perfectly cylindrical (R<<L)
Sausage has a homogeneous structure (Imre and Korney, 1990)
Sausage size and shape remain unchanged during drying and ripening
Weight loss is considered as the consequence of H2O evaporation only
Mass transfer is considered as the result of a H2O partial pressure difference between the outer surface of the sausage and air
Heat generation by fermentation is negligible
Heat transfer to sausage is under steady-state
All sausages have equal characteristics during drying

## Slide 46: SIMPLIFIED MODEL (lumped parameters): Equations
Mass balance equation
for a single sausage:
mds is mass of dry solid in kg
A is the sausage outer surface in m²
X is the moisture content of the sausage in kg (H2O)/kg (dry solid)
 is a mass transfer coefficient in kg/m2s
aw is the water activity corresponding to the equilibrium conditions with a humid solid
RH is the relative humidity of air
The desorption curve
The Oswin law is used:
 It is a first principles mathematical model.
It is also a dynamical model.
Notes: NEW

## Slide 47: SIMPLIFIED MODEL: Equations
Energy balance with the corresponding initial condition
[ACC] = IN - [OUT]
where:
· NR is the molar moisture flux at the surface [mol/(m2 s)]
· h is the convective heat transfer coefficient [kW/m2K]
· T is sausage temperature [K]
· Ta is air temperature [K]
· H(T) is the latent heat of water evaporation
· X is the moisture content on a dry basis (kg water/kg dry mass)
lumped parameters Eq.
Notes: DA aGGIUSTARE !

## Slide 48: SIMPLIFIED MODEL: Equations
Single sausage evaporation rate
The quantity of water which evaporates from the outer surface of a single sausage is given by:
Single sausage weight loss

## Slide 49: SIMPLIFIED MODEL: Numerical resolution
4th order Runge-Kutta Method to solve the differential equation
Trapezoidal rule to solve the following integral for weight loss
Implementation in Mathcad

## Slide 50: SIMPLIFIED MODEL: Results
Moisture content versus drying time
“Turista Buonpiemonte ” sausage
RH=0.8
Ta=20°C
va=0.6 m/s

## Slide 51: SIMPLIFIED MODEL: Results
Salami temperature versus drying time
“Turista Buonpiemonte” sausage
RH=0.8
Ta=20°C
va=0.6 m/s

## Slide 52: SIMPLIFIED MODEL: Results
Drying rate versus drying time
“Turista Buonpiemonte” sausage
RH=0.8
Ta=20°C
va=0.6 m/s

## Slide 53: Example No. 4 Modeling of salami drying
1st approach
lumped parameters
r [mm]
X [ kg (H2O/ kg (S.S.) ]
2nd approach
distributed parameters
Description of internal moisture profile
X [=] mass of H2O (liq.) / mass of dry solids
r [mm]
Notes: ---> presentation_MMPIA_2014-15.ppt

## Slide 54: COMPLETE MODEL (Distributed parameters approach – 1D): Equations
Water mass balance in a cylindrical shell
[IN] – [OUT] + [GEN] = [ACC]
where:
· D(X,T) is the mass diffusion coefficient depending on sausage moisture content and on sausage temperature (m2/s)
· X is the moisture content on a dry basis (kg water/kg dry mass)
 Radius is the only spatial coordinate
Lumped
Notes: new

## Slide 55: COMPLETE MODEL (Distributed parameters approach – 1D): Equations
Water mass balance, with the corresponding initial and boundary conditions
where:
· D(X,T) is the mass diffusion coefficient depending on sausage moisture content and on sausage temperature (m2/s)
· ds is the dry mass density (kg/m3)
· β is a mass transfer coefficient
0 R

1. parabolic, non-linear PDE
2. Neumann boundary conditions
Notes: DA Aggiungere energy balance !

## Slide 56: Mathematical Models 3rd classification
  Dynamical models
 Ch.3 of Himmelblau D.M. and Bischoff K.B., “Process Analysis and Simulation”, Wiley, 1967
on the base of
mathematical features of equations and variables,
also affecting type or easiness of solution
deterministic vs stocastic
lumped parameters vs distributed parameters
one dimension vs several dimensions
linear vs non linear
steady state vs time dependent
time-invariant vs time – varying
autonomous vs non – autonomous

## Slide 57: Example No.4 - COMPLETE MODEL (Distributed parameters approach – 1D): Geometrical domain
Notes: DA Aggiungere energy balance !

## Slide 58: Example No.4 - COMPLETE MODEL (Distributed parameters approach – 3D): Geometrical domain
3D plot of internal moisture content
Cylindrical geometry
Notes: DA Aggiungere energy balance !

## Slide 59: Example No.4 - COMPLETE MODEL (Distributed parameters approach – 3D): Geometrical domain
3D plot of internal moisture content
Irregular axial-symmetric geometry
Notes: DA Aggiungere energy balance !

## Slide 60: Example No.4 - COMPLETE MODEL (Distributed parameters approach – 3D): Geometrical domain
3D plot of internal moisture content
Irregular, non-axial-symmetric geometry
Notes: DA Aggiungere energy balance !

## Slide 61: Example No.4 - COMPLETE MODEL (Distributed parameters approach – 3D): Geometrical domain
3D plot of internal moisture content
Shrinking cylindrical geometry
Notes: DA Aggiungere energy balance !

## Slide 62: Mathematical Models 3rd classification
Several levels are possible:
Homogeneous vs. Inhomogeneous
Number of variables (e.g. binary and multicomponent systems)
Easy vs. difficult (subjective)
Constant coefficients vs. variable coefficients
Stiff system vs. non-stiff
Linear vs. non-linear system (algebraic and differential).
Order of differential equations (operators)
Ordinary differential equations, partial differential equations, differential-algebraic equations, integrodifferential equations etc.
Hyperbolic, parabolic and elliptic PDE
Initial vs. boundary value problem
Adapted from:
TEKNILLINEN KORKEAKOULU
  Differential models

## Slide 63: Mathematical Models 3rd classification
Homogeneous vs. inhomogeneous
  If f(x)= nf(x) for every , then f(x) is homogeneous to n:th degree.
Number of variables
  One-component system
  Two-component system
  Multi-component system
  More components, more degrees of freedom.
  Often one degree of freedom leads to scalar equations, more degrees to matrices.

## Slide 64: Mathematical Models 3rd classification
Easy vs. difficult:
  If this is estimated based on required time to solve the model with certain computational capacities, then this is actually a physical classification
Variable vs. constant coefficients:
Ex.:

## Slide 65: Mathematical Models 3rd classification
Stiff vs. non-stiff
  Formally, based on the ratio of eigenvalues
  In practice, if there are simultaneously very fast phenomena dictating step sizes, and very slow phenomena dictating simulation time, system is stiff.
Linear vs. non-linear
  In principle, linear systems are easy. Natural systems are rarely linear, but often numerical solution is based on (local) linearizations

## Slide 66: Linear Operator: Definition and first consequences
Formally, if V and W are vector spaces over the same ground field K, we say that f : V → W is a linear transformation if for any two vectors x and y in V and any scalar a in K, we have
  (additivity)
  (homogeneity).
This is equivalent to saying that f "preserves linear combinations", i.e., for any vectors x1, ..., xm and scalars a1, ..., am, we have (superposition)
1st example (linear)
f : w = a x
2nd example (non linear)
f : z = a2 b x y1/2
with a, b scalar constants
66
Notes: 66
NEW

## Slide 67: Linear Operator: Definition and first consequences
3rd example (non linear)
f : y = mx + p
with m, p scalar constants
67
NB:
It does not obey the principle of superposition
Notes: 67
Trasf. Conforme ???

## Slide 68: Mathematical Models 3rd classification
Several levels are possible:
Homogeneous vs. Inhomogeneous
Number of variables (e.g. binary and multicomponent systems)
Easy vs. difficult (subjective)
Constant coefficients vs. variable coefficients
Stiff system vs. non-stiff
Linear vs. non-linear system (algebraic and differential).
Order of differential equations (operators)
Ordinary differential equations, partial differential equations, differential-algebraic equations, integrodifferential equations etc.
Hyperbolic, parabolic and elliptic PDE
Initial vs. boundary value problem
Adapted from:
TEKNILLINEN KORKEAKOULU
  Differential models

## Slide 69: Mathematical Models 3rd classification
Order of differential equation
  It is defined as the order of the highest derivative in the differenzial eq.
  Ex.: n-th order ODE:
  Can be linear or non-linear, depending on parameters a and function f.
  If parameters a depend on x only (not on y), and function f is at most first order with respect to y, then the equation is linear
Order of a system of differential equation
It is defined as the sum of the orders of the individual eqns.
Notes: nuova

## Slide 70: Mathematical Models 3rd classification
Ordinary vs. partial differential equations
  ordinary: variables are functions of only one independent variable
  Ex.: Variable c is time invariant:   d
  partial: functions of several independent variables
  Ex.:Variable c depends on time and on position

## Slide 71: Mathematical Models 3rd classification
Differential-algebraic equations (DAE)
  In addition to the differential equations there are algebraic constraints.
  Ex.:
for variables x there are both differential and algebraic equations
for variables y there are only algebraic equations

## Slide 72: Mathematical Models 3rd classification
Integro-differential equations
  Involve both derivatives and integrals of the unknown variable.
  Ex.:
Distributed systems: x is a density distribution with respect to s, and this distribution depends on t.
K is sometimes called a Kernel function
  A reasonably general form:

## Slide 73: Mathematical Models 3rd classification
Initial vs. boundary value problems
Initial value problems usually easier: start from the initial values and ”march” forward in position or time.
Ex.:
the lumped parameters salami drying model
Boundary value problems are usually encountered in partial differential equations.
Ex.:
the distributed parameters salami drying model

## Slide 74: Linear-Lumped-Deterministic Models
 Introduction to Process Control Romagnoli & Palazoglu
“The theory of control is well developed for linear, deterministic, lumped-parameter models.”
Nonlinear
Distributed
Stochastic
Linear
Lumped
Deterministic
Simple!! But not necessarily the best…

## Slide 75: Mathematical Models 1st classification
  “First principle Models”
    Basic models
    Models involving trasport phenomena
    Models based on the “population balance approach”
  Empirical or “fitting” models
  Dynamic models
    input-output dynamic models
    input-state-output dynamic models or state-space models
    dynamic black box models
  Time Series
  Statistical models
(on the base of the approach adopted for model development)
 rielaborated from § 1.4 in Himmelblau D.M. e Bischoff K.B., “Process Analysis and Simulation”, Wiley & Sons Inc., 1967

## Slide 76: Dynamic Models: definitions
A dynamical system is a state space S , a set of times T and a rule R for evolution, R:S×T→S that gives the consequent(s) to a state s∈S .
  A dynamical system consists of an abstract phase space or state space, whose coordinates describe the state at any instant, and a dynamical rule that specifies the immediate future of all state variables, given only the present values of those same state variables.
  For example the state of a pendulum is its angle and angular velocity, and the evolution rule is Newton's equation F = ma.
A dynamical mathematical model can be considered to be a tool describing the temporal evolution of an actual dynamical system.
  Dynamical systems are deterministic if there is a unique consequent to every state, or stochastic or random if there is a probability distribution of possible consequents (the idealized coin toss has two consequents with equal probability for each initial state).
  A dynamical system can have discrete or continuous time.
Notes: NEW

## Slide 77: Dynamic Models: input-output representation
MATHEMATICAL MODEL
input output
 typical of automatic process control
 Roffel & Betlem, 2006
 Giua & Seatzu, “Analisi dei sistemi dinamici”, 2006
An input-output equation reveals the direct relationship between the output variable desired, and the input variable.
This relationship often includes the derivatives of one or both variables.
Even with a higher order equation, the advantage is that the output variable is independent of (uncoupled from) any other variables except the inputs.
vectorial scalar

## Slide 78: Example No.5 of input-state-output dynamic model: WATER OPEN TANK
IN :
STATE: h(t)
OUT :
h(t)
VARIABLES
Initial Condition: h(0) = h0
State equation:

## Slide 79: Input-Output representation Variables
Basic Automatic Control prof. Guariso
Notes: new

## Slide 80: Input-Output Models
General System Representation
(disturbances)
(parameters)
Process
1
d
2
d
L
d
1
m
…
…
2
m
K
m
:
:
1
a
2
a
R
a
1
y
2
y
J
y
(vectorial)
mathematical
model
(manipulated
variables)
(output
variables)
 typical of automatic process control
 Romagnoli & Palazoglu, Introduction to Process Control, 2005

## Slide 81: Definition of Linear dynamic system
From Wikipedia, the free encyclopedia: http://it.wikipedia.org
A linear dynamic system is a model based on some kind of linear operator H. Linear systems typically exhibit features and properties that are much simpler than the general, nonlinear case. By definition, they satisfy the properties of superposition and scaling:
  Given two inputs:
  i1(t), i2(t)
  as well as their respective outputs:
  y1(t) = H(i1(t))
  y2(t) = H(i2(t))
  then a linear system must satisfy:
  y1(t) + y2(t) = H( i1(t) +  i2(t))
  for any  and .

## Slide 82: Definition of Time-invariant system
Simple examples
To demostrate how to determine if a system is time-invariant then consider the two systems:
System A: yA(t) = ti(t)
System B: yB(t) = 10i(t)
Since system A explicitly depends on t outside of i(t) then it is time-variant. System B, however, does not depend explicitly on t so it is time-invariant.
Retrieved from Simple Systems by Don Johnson: http://cnx.org/content/m0006/latest/
Systems that don't change their input-output relation with time are said to be time-invariant.
The mathematical way of stating this property is to use the signal delay concept:.
y(t) =S(i(t) ) ⇒ y(t−τ) =S(i(t−τ) )
If you delay (or advance) the input, the output is similarly delayed (advanced). Thus, a time-invariant system responds to an input you may supply tomorrow the same way it responds to the same input applied today; today's output is merely delayed to occur tomorrow.
Retrieved from Wikipedia, the free encyclopedia: http://it.wikipedia.org
A time-invariant system is one whose output does not depend explicitly on time.
Notes: new

## Slide 83: Definition of Time-variant system
A time-variant system is one that is not time-invariant. The following things can be said about a time-variant system:
It has explicit dependence on time.
It is not stationary
 It does not have an impulse response (transfer function) in the normal sense. The system can be characterized by an impulse response except the impulse response must be known at each and every time instant.
Examples of time-variant systems
The human vocal tract is a time variant system, with its transfer function at any given time dependent on the shape of the vocal organs. As with any fluid-filled tube, resonances (called formants) change as the vocal organs such as the tongue and velum move. Mathematical models of the vocal tract are therefore time-variant, with transfer functions often linearly interpolated between states over time.
Notes: NEW

## Slide 84: Table of Typical Math Operators
Input-Output Relation | Linear | Time-Invariant
y(t) = d/dt [x(t)] | yes | yes
y(t) = d2/dt2 [x(t)] | yes | yes
y(t) = (d/dt [x(t)])2 | no | yes
y(t) = d/dt [x(t)]+ x(t) | yes | yes
y(t) = x1+x2 | yes | yes
y(t) = x(t−τ) | yes | yes
y(t) = cos(2πft) x(t) | yes | no
y(t) = x2(t) | no | yes
y(t) = ¦x(t) ¦ | no | yes
y(t) = mx(t) +b | no | yes
Retrieved from:
http://cnx.rice.edu/content/m0006/latest/
y(t) = x(−t) | yes | no

## Slide 85: Definition of Autonomous system (in theory of differential equations)
 Retrieved from Luenberger, Introduction to Dynamic Systems
A system of ODEs is called autonomous or time invariant if its vector field does not depend explicitly on time.
Retrieved from "http://en.wikipedia.org/wiki/Autonomous_system_%28mathematics%29"
An autonomous system is an ODE equation of the form
where x takes values in n-dimensional Euclidean space and t is usually time. It is distinguished from systems of differential equations of the form
in which the law governing the rate of motion of a particle depends not only on the particle's location, but also on time; such systems are not autonomous.
Simple examples
System A:
System B:
Since system A explicitly depends on t outside of x(t) then the dynamic system is not autonomous. System B, however, does not depend explicitly on t so it is autonomous.
Vector field
Notes: new

## Slide 86: Mathematical Models 1st classification
  “First principle Models”
    Basic models
    Models involving trasport phenomena
    Models based on the “population balance approach”
  Empirical or “fitting” models
  Dynamic models
    input-output dynamic models
    input-state-output dynamic models or state-space models
    dynamic black box models
  Time Series
  Statistical models
(on the base of the approach adopted for model development)
 rielaborated from § 1.4 in Himmelblau D.M. e Bischoff K.B., “Process Analysis and Simulation”, Wiley & Sons Inc., 1967

## Slide 87: Dynamic Models: input-state-output representation
MATHEMATICAL MODEL
Input state output
 Giua & Seatzu, “Analisi dei sistemi dinamici”, 2006
     Behavioral models
     “internal” model of the process
     Roffel & Betlem, 2006
Intuitively, the state of a system describes enough about the system to determine its future behavior.
vectorial scalar

## Slide 88: Definition of State
  The state of a dynamic system is defined through the smallest set of variables (called the state variables) such that the knowledge of these variables at t=t0, together with the knowledge of the input for tt0, completely determines the behavior of the system for any time.
Introduction to Process Control Romagnoli & Palazoglu
State variable  x(t)
Notes: new

## Slide 89: Input-state-output model
Basic Automatic Control prof. Guariso
 Such a “memory”, required to define the present-time condition of the system, is called the state of the system at the time instant when the input is applied.

## Slide 90: Example No.5 of input-state-output dynamic model: WATER OPEN TANK
h(t)
IN :
STATE: h(t)
OUT :
VARIABLES:
Initial Condition:
State equation:
Output transformation:
h(0) = h0
Notes: new

## Slide 91: VARIABLES
Variables are things that vary and change

## Slide 92: VARIABLES Classification in dynamic models
INPUT:
time-varying quantities that change according to a known or prefixed law.
The user (e.g., manipulated variables) or the outside environment (e.g., disturbances) decides how they change with time
OUTPUT:
quantities representing the observed or calculated time-varying results that the model yields to outside.
They are originally unknown, but provide (typically as functions) results to outside once the input variables have been specified and the state variables have been calculated.

## Slide 93: State Variables
Quantities describing the present state of a system enough well to determine its future behavior.
They provide a means to keep memory of the consequences of the past inputs to the system.
They may be partly coincident with output variables.
The minimum number of state variables required to represent a given system, n, is usually equal to the order of the system's defining differential equation.
The choices for variables to include in the state is highly dependent on the fidelity of the model and the type of system.
One can see immediately that the choice of variables to be included in the state is not unique.
 HINT: The state variables are often given by the same variables appearing within the initial conditions of the system’s ODEs
Basic Automatic Control prof. Guariso
http://www.cds.caltech.edu/~murray/amwiki/index.php/FAQ:_What_is_a_state%3F_How_does_one_determine_what_is_a_state_and_what_is_not%3F

## Slide 94: State Variables
Basic Automatic Control prof. Guariso

## Slide 95: State-Space Models
Basic Automatic Control prof. Guariso

## Slide 96: State-Space Models
Basic Automatic Control prof. Guariso

it is a scalar model (n = 1)
6
Notes: new

## Slide 97: Example No.7: Pasteurized Milk Storage (Two Non-interacting Tanks)
F0
F1
F2
With a constant cross sectional
area A, the volume of a tank can be expressed as:
V = Ah
where h represents the liquid level.
Let us suppose that the control objective is to maintain a constant level in the second tank while the inlet flow rate to the first tank is varied.
The liquid level h2(t) is the variable that we want to be the controlled variable.
Introduction to Process Control Romagnoli & Palazoglu
Notes: new

## Slide 98: Example No.7 – Two (Non-interacting) Tanks State-space Model
Defining:
State-space process model
Introduction to Process Control Romagnoli & Palazoglu
IC:
h1(0)=h1s , h2(0)=h2s
mass balances constitutive eqs.
Notes: NEW

## Slide 99: Example No.7 – Two (Non-interacting) Tanks State-space Model
Introduction to Process Control Romagnoli & Palazoglu
MODEL CLASSIFICATION:
DYNAMIC, LINEAR, CONSTANT-COEFFICIENT, NON-AUTONOMOUS, TIME-INVARIANT, 2 ODE SYSTEM.
ORDER = 2
vector field
Notes: NEW

## Slide 100: State-space Models Terminology
nN is the order or size of the model
x(t) is the vector of the state variables
The n components of x(t) are phases
The space spanned x(t) n is the state-space or phase-space
u(t) is the vector of the input variables with m components
The function f:·+ · n ·m →n is the vector field

## Slide 101: Linear State-space Models Terminology
A is the is the state matrix (nn)
B is the is the input matrix (nm)
Initial Condition:
State equation:
Output
transformation:
Notes: new

## Slide 102: Autonomous System (definition in Theory of Systems)
An autonomous system is a system having the state not depending on input
OR
input constant with time
in its the mathematical model.
adapted from “notecontrolli_PRATTICHIZZO.pdf”
NB:
For a dynamic model described by a system of ODEs, an autonomous system is also time invariant
Notes: new

## Slide 103: Autonomous System (in Non-Linear Dynamics )
A dynamic system is autonomous if its vector field depends on the state x(t), but does not explicitly depend on time.
Examples of 2nd order systems:
Autonomous system Non-autonomous system
with x(t)n
t +

## Slide 104: Example No.7 – Two (Non-interacting) Tanks State-space Model
Introduction to Process Control Romagnoli & Palazoglu
State-space (linear) process model
State matrix
Input matrix
State variables
Output variable
MODEL CLASSIFICATION:
DYNAMIC, LINEAR, NON-AUTONOMOUS, TIME-INVARIANT, 2 ODE SYSTEM.
ORDER = 2
Notes: 104
new

## Slide 105: Orbits or Trajectories of a dynamic system
The forward orbit or trajectory of a state x is the time-ordered collection of states that x follow from an initial state x0 using the system evolution rule.
When both state space and time are continuous, the forward orbit is a curve x(t) parametric in t ≥ 0
Different initial states result in different trajectories
Example of an orbit (order n=2)
x1
x2

## Slide 106: Phase portrait
The set of of all trajectories forms the phase portrait of a dynamical system.
in practice, only representative trajectories are considered
the phase portrait is usually built by numerical methods for nonlinear systems
The analysis of phase portraits provides an extremely useful way for visualizing and understanding qualitative features of solutions.
The phase portrait is particolarly useful for scalar (1st order) and planar systems (2nd order)
x1
x2
Notes: NEW

## Slide 107: Transients and regimes
The orbits may have a bounded or unbounded asymptotic behavior (for t  ± ).
If an orbit has a bounded asymptotic behavior for t  + , the part of the orbit describing such an asymptotic behavior is referred to as regime and the remaining part is referred to as transient.
The simplest and most well known regime (bounded) is the equilibrium point (steady-state point), which is possible for every system order n
Notes: NEW

## Slide 108: Stability of an equilibrium point
For example,
the equilibrium of a pencil standing on its tip is unstable;
the equilibrium of a picture on the wall is (usually) stable;
the equilibrium of a ball on a flat plane is (usually) indifferent.
Adapted fromOn-Line Lectures ©Alexei Sharov, Department of Entomology, Virginia Tech, Blacksburg, VA http://www.ento.vt.edu/~sharov/PopEcol/
 More formal definitions of stability do exist …
An equilibrium may be stable or unstable or indifferent.

## Slide 109: Example No.7 – Two (Non-interacting) Tanks Input-Output Model
A single equation describing the effect of the input on the output.
substituting
Finally,
Introduction to Process Control Romagnoli & Palazoglu
substituting
differenziating
m(t)
y(t)

## Slide 110: Mathematical Models 4th classification
(based on the type of description adopted for time as the independent variable)
 VALID for DYNAMICAL SYSTEMS only
continuous time models
discrete time models

## Slide 111: CONTINUOUS-TIME SYSTEMS
The time changes continuously. It is not possible to define a minimum time interval: it is always possible to consider a smaller time interval.
Accordingly, the theory of continuous-time systems has been defined and studied, where the variables of the system are continuous-time functions, that is, at every time instant t, it is possible to define and assign the variable value.
Continuous-time systems: t  ℜ

## Slide 112: DISCRETE-TIME SYSTEMS
Ingresso uscita
Input output
input – output representation
MATHEMATICAL MODEL
input – state – output representation
MATHEMATICAL MODEL
Ingresso stato uscita
Input state output

## Slide 113: DISCRETE-TIME SYSTEMS
EXPLICIT TYPE
“IMPLICIT” TYPE
General representation
of input–state–output discrete-time models
SCALAR SYSTEMS: x(k) is a scalar variable
VECTOR SYSTEMS: x(k) is a vector variable of size n
   A deterministic system with discrete time is often defined a map.

## Slide 114: Example No. 1 Malthusian Growth Model (II)
If we let x(k) denote the population size during time period k and let c denote the population growth rate per unit time, the Malthusian model can be written mathematically in the following way:
x(k+1) = (1+c) x(k)
A model in this form, where the population at the next time period is determined by the population at the previous time period, is said to be a
difference equation model or a map.
The initial condition is:
IC: x(0) = x0
autonomous discrete-time system of order 1 (scalar model)
Notes: NEW

## Slide 115: Model Order
The order n is an integer number obtained as the product between the size of the state vector x and the time gap in the implicit model representation.
 The time gap is the max time distance in the implicit model representation
Example 1:
autonomous discrete-time system of order 1 (scalar model)
Example 2:
autonomous discrete-time system of order 2 (vectorial model)

## Slide 116: Fixed Points for autonomous systems x(k+1) = f(x(k)
DEFINITION of a fixed point:
x(k+1) = x(k)
 x(k) may be a scalar or vector variable
DETERMINATION of a fixed point:
The fixed points are determined as the solutions of the algebraic eq. (scalar) or system of eqns.(vector):
x*= f (x*)
A fixed point can be stable or unstable.
A stable fixed point is an attractor for the trajectories originating in a reasonable neighborhood of it.
Notes: NEW

## Slide 117: Orbits or Trajectories
Example:
autonomous non-linear, discrete-time model of order 2
fixed point
initial condition

## Slide 118: Example No. 2 Logistic Model
Differently from the Malthusian model …
developed by Belgian mathematician Pierre Verhulst (1838)
HYPOTHESES
resources are limited for growth: N(t)≤Nsat
CLOSED-FORM SOLUTION
N0≠0
Nsat
Notes: NEW

## Slide 119: Example No. 2 Logistic Map
adimen-
siona-lization
discreti-zation

## Slide 120
  Modelli a “principi primi” (“First principle Models”)
    Modelli basati sui “fenomeni di trasporto”
  Modelli basati sul “bilancio di popolazione”
  Modelli empirici o di “fitting”
  Dynamic models
    input-output dynamic models
    input-state-output dynamic models or state-space models
    dynamic black box models
  Serie temporali
  Modelli stocastici
120
(on the base of the approach adopted for model development)
Mathematical Models 1st classification
Notes: 120

## Slide 121: Black-Box Model Structures
The model structures vary in complexity and order depending on the flexibility you need to account for the dynamics and on possible consideration of noise in your system.
The simplest black-box structures are:
Linear polynomial model, which is the simplest input-output model (e.g., ARX model)
Transfer function, with a given number of adjustable poles and zeros.
State-space model, with unknown system matrices, which you can estimate by specifying the number of model states
Non-linear parameterized functions
121
Input output
BLACK BOX
MODEL
Notes: Trovare la fonte della slide
Spostare e discutere ARX
121

## Slide 122: Black-Box Modeling
Black-box modeling is usually a trial-and-error process, where you estimate the parameters of various structures and compare the results.
Typically, you start with the simple linear model structure and progress to more complex structures.
You might also choose a model structure because you are more familiar with this structure or because you have specific application needs.
122
Black box models are not based on physical grounds and the equations do not reflect the internal structure of the process.
Black box models usually have a linear structure, and because of this built-in linearity they have a limited validity range.
Notes: 122

## Slide 123: Dynamic black box. Linear polynomial models
123
Black box models may describe the system dynamics through a linear, time-invariant vector difference equation of finite dimension.
The difference equation has some model parameters.
The following difference equation represents a simple model structure:
where a and b are adjustable parameters.
Parameters are a crucial point in dynamic black box model development.
In order to parameterize a black box model, only the input-output behavior is required; detailed knowledge about the internal behavior is not necessary.
The parameters are estimated by minimizing a scalar function of the prediction error, i.e. the difference between the observed output and the model-predicted output.
Notes: new
123

## Slide 124: Example No.8 the ARMAX model
124
where:
y(t) represents the output at time t,
u(t) represents the input (eXogenous variable) at time t,
na is the number of poles for the dynamic model,
nb is the number of zeros plus 1,
nc is the number of poles for the disturbance model,
nk is the dead time (in terms of the number of samples) before the input affects output of the system,
e(t) is the white-noise disturbance (gaussian)
here t≅k
the ARMAX model is NOT deterministic
For a single-input/single-output system (SISO), the ARMAX (Auto-Regressive Moving-Average with eXogenous variable) model structure is:
Auto-Regression
Moving-Average
Notes: 124

## Slide 125: System Identification
125
System identification is a methodology for building mathematical models of dynamic systems using measurements of the system's input and output signals/data.
The process of system identification requires that you:
Measure the input and output signals/data from your system in time or frequency domain.
Select a model structure.
Apply an estimation method to estimate value for the adjustable parameters in the candidate model structure.
Evaluate the estimated model to see if the model is adequate for your application needs.
System identification uses the input and output signals you measure from a system to estimate the values of adjustable parameters in a given model structure.
Obtaining a good model of your system depends on how well your measured data reflect the behavior of the system.
Documentation center
Notes: new
125

## Slide 126
  Modelli a “principi primi” (“First principle Models”)
    Modelli basati sui “fenomeni di trasporto”
  Modelli basati sul “bilancio di popolazione”
  Modelli empirici o di “fitting”
  Dynamic models
    input-output dynamic models
    input-state-output dynamic models or state-space models
    dynamic black box models
  Serie temporali
  Modelli stocastici
126
(on the base of the approach adopted for model development)
Mathematical Models 1st classification
Notes: 126

## Slide 127: Dynamical modeling Final Statement
127
A way to distinguish the techniques used when modeling dynamic processes is to picture them on a scale with two extremes at the ends:
at the one side black box system identification
at the other side theoretical modeling or first principles modeling
Notes: 127

## Slide 128: Mathematical Models 5th classification
  1. ANALYTICAL SOLUTIONS  DIFFERENTIAL CALCULUS
       ALGEBRA
2. NUMERICAL SOLUTIONS  NUMERICAL CALCULUS
      Ex.: numerical methods for PDEs
  FINITE DIFFERENCE METHODS (FDM)
  FINITE ELEMENT METHODS (FEM)
  COLLOCATION METHODS
(based on the type of solution,
with exclusion of empirical models)

## Slide 129
  Modelli a “principi primi” (“First principle Models”)
    Modelli basati sui “fenomeni di trasporto”
  Modelli basati sul “bilancio di popolazione”
  Modelli empirici o di “fitting”
  Modelli dinamici
    Modelli dinamici “con rappresentazione ingresso-uscita”
    Modelli dinamici “con rappresentazione nello spazio di stato”
    Modelli dinamici a scatola nera (black box)
  Time Series
  Modelli stocastici
(on the base of the approach adopted for model development)
Mathematical Models 1st classification