## Slide 1: Overview on Mathematical Modeling
Prof. Ing. Michele MICCIO
Dept. of Industrial Engineering (Università di Salerno)
Prodal Scarl (Fisciano)
Rev. 7.5 of June 3, 2019
Notes: 1

## Slide 2: TYPES OF MODELS
Models are used not only in the natural sciences (such as physics, biology, earth science, meteorology) and engineering/architecture disciplines, but also in the social sciences (such as economics, psychology, sociology and political science) and in public administration activities.
Here is a list:
· Physical Models
· Analogic Models
· Provisional Theories (e.g., molecular and atomic models)
· Maps and Drawings (e.g., PI&D, geographycal maps, etc.)
· Mathematical and symbolic models
 § 1.4 in Himmelblau D.M. e Bischoff K.B., “Process Analysis and Simulation”, Wiley & Sons Inc., 1967

## Slide 3: MATHEMATICAL MODELS Definitions
A mathematical model is a representation, in mathematical terms, of certain aspects of a non-mathematical system.
Aris, 1999
A mathematical model is a set of mathematical equations that are intended to capture the effect of certain system variables on certain other system variables.
G. C. Goodwin, St. F. Graebe, M. E. Salgado, Control System Design, Ch. 3, Prentice Hall , 2001
A model may be prescriptive or illustrative, but, above all, it must be useful !
Wilson, 1991

## Slide 4: MATHEMATICAL MODELS Definitions
A mathematical model is a description of a system using mathematical concepts and language.
. . .
A mathematical model usually describes a system by a set of variables and a set of equations that establish relationships between the variables.
. . .
Mathematical models are used not only in the natural sciences (such as physics, biology, earth science, meteorology) and engineering disciplines (e.g. computer science, artificial intelligence), but also in the social sciences (such as economics, psychology, sociology and political science); physicists, engineers, statisticians, operations research analysts and economists use mathematical models most extensively.
A model may help to explain a system and to study the effects of different components, and to make predictions about behavior.

## Slide 5: MATHEMATICAL MODELING Definition
The (human) process of developing a mathematical model is termed mathematical modelling.

## Slide 6: WHY MATH MODELING FOR PROCESS SYSTEMS?
Is it:
  to design a controller?
  to analyze the performance of the process?
  to understand the process better?
  to simplify the complexity of a system
  etc.
Introduction to Process Control Romagnoli & Palazoglu

## Slide 7: SIMULATION
The study of a system (also including a real-world process, event or phenomenon) that is performed by means of its mathematical model.
Simulation is usually carried out through a suitable software code implementing the mathematical model.
For example,
simulation may imply
search of a model solution,
value and meaning of output variables,
pattern of a dynamic response,
use of adjustable parameters,
etc.
Notes: NEW

## Slide 8: VALIDATION
In modeling and simulation, validation is the (human) process of determining the degree to which a model or a simulation carried out with the model is an accurate representation of the real world from the perspective of the intended uses.
From 
http://www.thefreedictionary.com
Notes: NEW

## Slide 9: THE MATHEMATICAL MODELING CYCLE
Modello
F = m × a
        ft tt re 12 14 tf 13 15
Costruzione modello
Ricerca della soluzione
Interpretazione della soluzione
Mondo Reale
Donatella Sciuto, Giacomo Buonanno e Luca Mari - Introduzione ai sistemi informatici, 5a ed.
Notes: DA AGGIUSTARE

## Slide 10: MATHEMATICAL MODELS 1st CLASSIFICATION
  “First principle Models”
    Basic models
    Models involving trasport phenomena
    Models based on the “population balance approach”
  Empirical or “fitting” models
  Dynamic models
    dynamic models with “input-output rappresentation”
    state-space dynamic models
    black box dynamic models
  Time Series
  Statistical models
Deterministic Models
 rielaborated from § 1.4 in Himmelblau D.M. e Bischoff K.B., “Process Analysis and Simulation”, Wiley & Sons Inc., 1967
Framework: general
Approach adopted for model development

## Slide 11: MATHEMATICAL MODELS 1st CLASSIFICATION
  First principles Models
  or Fundamental Models ( Palazoglu & Romagnoli, 2005) or Mechanistic or White Box Models ( Roffel & Betlem, 2006)
  Modelli empirici o di “fitting”
  Modelli dinamici
    Modelli dinamici “con rappresentazione ingresso-uscita”
    Modelli dinamici “con rappresentazione nello spazio di stato”
    Modelli dinamici a scatola nera (black box)
  Serie temporali
  Modelli statistici
(on the base of the approach adopted for model development)

## Slide 12: GENERAL CONSERVATION LAW
It is the most well known example of a Fundamental Principle:
Input - Output + Net Generation = Accumulation
NB: GEN > 0  formation
GEN < 0  disappearance
SIMPLER CASES
For a chemical element:
IN - OUT = ACC
At steady-state:
IN - OUT + GEN = 0
At steady-state and without chemical/biochemical reactions:
IN - OUT = 0
 see also Stephanopoulos, ch. 4
Notes: New

## Slide 13: FIRST PRINCIPLES MODELS
The description of such a system and the development of such a model require the concept of:
control volume
or
system boundary
 This holds also for the case of population balance models
Notes: new

## Slide 14: MATHEMATICAL MODELS 1st CLASSIFICATION
  “First principles Models”
    Basic models
    Models involving transport phenomena
    Models based on the “population balance approach”
  Empirical or “fitting” models
  Dynamic models
    dynamic models with “input-output representation”
    state-space dynamic models
    black box dynamic models
  Time Series
  Statistical models
 rielaborated from § 1.4 in Himmelblau D.M. e Bischoff K.B., “Process Analysis and Simulation”, Wiley & Sons Inc., 1967
(on the base of the approach adopted for model development)
Notes: NEW

## Slide 15: FIRST PRINCIPLES MATHEMATICAL MODELS. Malthusian Growth Model
An Early and Very Famous Population Model
In 1798 the Englishman Thomas R. Malthus posited a mathematical model of population growth. He model, though simple, has become a basis for most future modeling of biological populations. His essay, "An Essay on the Principle of Population," contains an excellent discussion of the caveats of mathematical modeling and should be required reading for all serious students of the discipline. Malthus's observation was that, unchecked by environmental or social constraints, it appeared that human populations doubled every twenty-five years, regardless of the initial population size. Said another way, he posited that populations increased by a fixed proportion over a given period of time and that, absent constraints, this proportion was not affected by the size of the population. By way of example, according to Malthus, if a population of 100 individuals increased to a population 135 individuals over the course of, say, five years, then a population of 1000 individuals would increase to 1350 individuals over the same period of time.
Malthus's model is an example of a model with one variable and one parameter.
A variable is the quantity we are interested in observing. They usually change over time.
Parameters are quantities which are known to the modeler before the model is constructed. Often they are constants, although it is possible for a parameter to change over time. In the Malthusian model the variable is the population and the parameter is the population growth rate.

## Slide 16: Example No. 1 Malthusian Growth Model
PARAMETERS
STATE VARIABLES
MATHEMATICAL CLASSIFICATION
dynamic, autonomous mathematical model
made by 1 ODE (Order =1),
linear, homogeneous, constant coefficient equation
GENERAL CONSERVATION LAW applied to No. of individuals in a “closed system”: ACC = GEN
GEN = birth - death
INITIAL CONDITION:

## Slide 17: Example No. 2 Logistic Model
Differently from the Malthusian model …
developed by Belgian mathematician Pierre Verhulst (1838)
HYPOTHESES
resources are limited for growth: N(t)≤Nsat
GENERAL CONSERVATION LAW applied to No. of individuals in a “closed system”: ACC = GEN GEN = birth - death
PARAMETERS
STATE VARIABLES
MATHEMATICAL CLASSIFICATION
Dynamic, autonomous mathematical model
made by 1 ODE (Order =1) ,
non linear, homogeneous, constant coefficient equation
Notes: NEW

## Slide 18: Example No. 2 Logistic Model
resources are limited for growth: N(t)≤Nsat
CLOSED-FORM SOLUTION
N0≠0
Nsat
Notes: NEW

## Slide 19: MATHEMATICAL MODELS 1st CLASSIFICATION
  “First principle Models”
    Basic models
    Models involving transport phenomena
    Models based on the “population balance approach”
  Empirical or “fitting” models
  Dynamic models
    dynamic models with “input-output rappresentation”
    state-space dynamic models
    black box dynamic models
  Time Series
  Statistical models
 rielaborated from § 1.4 in Himmelblau D.M. e Bischoff K.B., “Process Analysis and Simulation”, Wiley & Sons Inc., 1967
(on the base of the approach adopted for model development)

## Slide 20: TRANSPORT PHENOMENA
Examples:
Newton law of viscosity
Fourier law of heat conduction
1st Fick law of diffusion
General Law
(flux) = (transfer coefficient)・(spacial gradient)

## Slide 21: TRANSPORT AND KINETIC RATE EQUATIONS
Momentum, Heat and Mass transfers
 | Heat | Mass | Momentum
Flux | q | nA | τxy
Diffusion transfer (microscopic scale) |  |  | 
Law | Fourier’s law | 1st Fick’s law | Newton’s law
Driving force (gradient) | dT/dx | dCA/dx | dvy/dx
Key parameter (transfer coefficient) | kT (Thermal conductivity) | DAB (Binary Diffusivity) | µ (Viscosity)
Convection transfer (macroscopic scale) |  |  | 
Driving force | ∆T | ∆CA | ∆P

## Slide 22: Example No. 3 The Tubular Reactor
VARIABILI
x: ascissa, m
t: tempo, s
u: velocità, m/s
C: concentrazione del reagente, mol/m3
D: diffusività assiale del gas, m2/s
k: cost. reazione 2° ordine, m3/moli/s
dx
u
0
L
x
An example of a first principles model involving transport phenomena.
HYPOTHESES
Isothermal reactor
2nd order homogeneous chemical reaction
A → P
Flat velocity profile
Axial diffusion only
Notes: NEW

## Slide 23: Example No. 3 The Tubular Reactor
E' un'equazione differenziale alle derivate parziali (PDE) quasi-lineare, parabolica del secondo ordine, integrabile per assegnate condizioni iniziali e condizioni al contorno
(DIFFERENTIAL) MASS BALANCE
ACC = IN – OUT + GEN
Notes: NEW

## Slide 24: Example No. 3 The Tubular Reactor
initial condition
boundary conditions
x = 0
x = L
Boundary and initial conditions

## Slide 25: MATHEMATICAL MODELS 1st CLASSIFICATION
  “First principle Models”
    Basic models
    Models involving transport phenomena
    Models based on the “population balance approach”
  Empirical or “fitting” models
  Dynamic models
    dynamic models with “input-output rappresentation”
    state-space dynamic models
    black box dynamic models
  Time Series
  Statistical models
 rielaborated from § 1.4 in Himmelblau D.M. e Bischoff K.B., “Process Analysis and Simulation”, Wiley & Sons Inc., 1967
(on the base of the approach adopted for model development)

## Slide 26
MODELS BASED ON A “POPULATION BALANCE APPROACH”
Formulation
The Population Balance Equation was originally derived in 1964, when two groups of researchers studying crystal nucleation and growth recognized that many problems involving change in particulate systems could not be handled within the framework of the conventional conservation equations only, see Hulburt & Katz (1964) and Randolph (1964).
They proposed the use of an equation for the continuity of particulate numbers, termed population balance equation, as a basis for describing the behavior of such systems.
This balance is developed from the general conservation law:
Input - Output + Net Generation = Accumulation
 § 4.4 in Himmelblau D.M. and Bischoff K.B., “Process Analysis and Simulation”, John Wiley & Sons Inc., 1967 (Collocazione: 660.281 HIM 1)

## Slide 27
ELEMENTS NECESSARY FOR A POPULATION BALANCE MODEL

## Slide 28
ENTITY DISTRIBUTION FUNCTION
Physical meaning
is the fraction of entities at time t that are:
contained in the infinitesimal volume dV=dxdydz
characterized by values of properties in the ranges ζ1÷ζ1+dζ1, . . . , ζm÷ζm+dζm

## Slide 29: MATHEMATICAL MODELS 2nd CLASSIFICATION
Structured Models (or Theoretical or White Box Models)
Unstructured Models (or Empirical or Black Box Models)
Hybrid Models (or Gray Box Models)
Framework: process systems
Approach of process engineering
 Ogunnaike B.A. and Ray W.H., “Process Dynamics, Modeling and Control”, Oxford Univ. Press, 1994
 Romagnoli & Palazoglu, "Introduction to Process Control"

## Slide 30: STRUCTURED MODELS
Characteristics:
Mathematical equations describing the process system can be:
a) Conservation equations e.g. total mass, mass of individual chemical species, total energy, momentum and number of particles.
b) Rate equations e.g. transport rate and reaction rate equation.
c) Equilibrium equation e.g. reaction and phase equilibrium.
Equations of state e.g. ideal gas law
Other constitutive relationships, e.g., control valve flow equation, PID control law, etc.
 Advantages:
They provide fundamental and general knowledge of the process
 Disadvantages:
They require a good and reliable understanding of the physical and chemical phenomena that underlie the process
Accuracy of models depends on the assumptions and mathematical ability of the person constructing the model.
white box
Model
i
y

## Slide 31: UNSTRUCTURED MODELS
Characteristics:
They rely on measured or observed data availability:
  a) Vary input variables and then measure the value of the output variables.
  b) Perform enough measurements or observations (experiments)
The equations describing a process system in this way consist in mathematical relationships among the variables representing the available data (fitting).
Such models that rely solely on empirical information are termed as black-box models.
Example: A black-box model simulating the internal combustion engine operation and implemented into the control box of a modern car
 Advantages:
a) No or very limited assumptions required.
b) Just focus on the range of process operating conditions.
 Disadvantages:
a) They require an actual operating process and may become very time-consuming and costly
b) They don’t allow extrapolation, generally
c) They never give the engineer a fundamental understanding of the process.
black box
Model
i
y

## Slide 32: Example 4 FOPDT model
where:
y(t) is the measured process variable
u(t) is the controller output signal
The important parameters that result are:
      Steady State Process Gain, KP
      Overall Process Time Constant, P
      Apparent Dead Time, P or td
 The FOPDT model is low order and linear: so it can only approximate the behavior of real processes
adapted from:
D. Cooper, "Practical Process Control using Loop-Pro Software", PDF textbook
An example of Black-Box Dynamic Model
Modeling means fitting a first order plus dead time (FOPDT) dynamic process model to the data set:

## Slide 33: STRUCTURED AND UNSTRUCTURED MODELS: a comparison
Structured Models theory-rich and data-poor
Unstructured Models data-rich and theory-poor

## Slide 34: “HYBRID” MODELS
Hybrid Model is developed by incorporating empirical knowledge into the fundamental understanding of the process.
Such models blending fundamental and empirical knowledge are referred to as gray-box models.
  Example
  An example can be the use of mass and energy balances to develop a reactor model and the rate of the reaction will be based on an empirical expression obtained from laboratory experiments.
Introduction to Process Control Romagnoli & Palazoglu
gray box
Model
i
y

## Slide 35: MATHEMATICAL MODELS 1st CLASSIFICATION
  “First principle Models”
    Basic models
    Models involving transport phenomena
    Models based on the “population balance approach”
  Empirical or “fitting” models
  Dynamic models
    dynamic models with “input-output rappresentation”
    state-space dynamic models
    black box dynamic models
  Time Series
  Statistical models
 rielaborated from § 1.4 in Himmelblau D.M. e Bischoff K.B., “Process Analysis and Simulation”, Wiley & Sons Inc., 1967
(on the base of the approach adopted for model development)
Notes: NEW

## Slide 36
EMPIRICAL OR “FITTING” MODELS
Mathematical models obtained by curve fitting
Curve fitting is the process of constructing a curve, or mathematical function, that has the best fit to a series of data points, possibly subject to constraints.
Curve fitting can involve:
  either interpolation, where an exact fit to the data is required,
  or smoothing, in which a "smooth" function is constructed that approximately fits the data.
A related topic is regression analysis, which focuses more on questions of statistical inference such as how much uncertainty is present in a curve that is fit to data observed with random errors.
Fitted curves can be used as an aid for
  to visualize data, e.g., to infer values of a function where no data are available,
  and to summarize the relationships among two or more variables.
Extrapolation refers to the use of a fitted curve beyond the range of the observed data, and is subject to a greater degree of uncertainty since it may reflect the method used to construct the curve as much as it reflects the observed data.

## Slide 37
EMPIRICAL OR “FITTING” MODELS
The interpolation problem
The smoothing or
regression problem

## Slide 38: MATHEMATICAL MODELS 3rd CLASSIFICATION

Ch.3 of Himmelblau D.M. and Bischoff K.B., “Process Analysis and Simulation”, Wiley, 1967
http://www.csd.newcastle.edu.au//chapters/chapter3.html
on the base of
mathematical features of equations and variables,
also affecting type or easiness of solution
  with ref. to Dynamical Models
Model attribute | Contrasting attribute | Asserts whether or not ...
Deterministic | Stochastic | ...the model equations have no stochastic variables or at least one
Lumped parameter | Distributed parameter | ...the model-predicted variables are a function of the spatial variables or not
Single input single output | Multiple input multiple output | ...the model equations have one input and one output only
One dimension | Several dimensions | ...the model equations have one or more independent spatial variables
Linear | Nonlinear | ... the model equations are linear in the system variables
Steady state | Time dependent OR dynamic | … time is one of the independent variables
Time invariant | Time varying | ... model parameters or coefficients in equations do not change with time
Continuous | Sampled | ...model equations describe the behavior at every instant of time, or only in discrete samples of time
Notes: Da completare!

## Slide 39: MATHEMATICAL MODELS 3rd CLASSIFICATION
 Romagnoli & Palazoglu, “Introduction to Process Control”
Linear system
any function or term in the model equations must satisfy two basic properties:
additivity
homogeneity
Nonlinear
Distributed
Stochastic
Linear
Lumped
Deterministic
Simple!!
But not necessarily the best…
Viewpoint of process engineering
The theory of control is well developed for linear, deterministic, lumped-parameter models (see Transfer Functions).

## Slide 40: MATHEMATICAL MODELS 1st CLASSIFICATION
  “First principle Models”
    Basic models
    Models involving transport phenomena
    Models based on the “population balance approach”
  Empirical or “fitting” models
  Dynamic models
    input-output dynamic models
    input-state-output dynamic models or state-space models
    dynamic black box models
  Time Series
  Statistical models
 rielaborated from § 1.4 in Himmelblau D.M. e Bischoff K.B., “Process Analysis and Simulation”, Wiley & Sons Inc., 1967
(on the base of the approach adopted for model development)

## Slide 41: DYNAMIC MODELS: definitions
A dynamical system is a state space S , a set of times T and a rule R for evolution, R:S×T→S that gives the consequent(s) to a state s∈S .
  A dynamical system consists of an abstract phase space or state space, whose coordinates describe the state at any instant, and a dynamical rule that specifies the immediate future of all state variables, given only the present values of those same state variables.
  For example the state of a pendulum is its angle and angular velocity, and the evolution rule is Newton's equation F = ma.
A dynamical mathematical model can be considered to be a tool describing the temporal evolution of an actual dynamical system.
  Dynamical systems are deterministic if there is a unique consequent to every state, or stochastic or random if there is a probability distribution of possible consequents (the idealized coin toss has two consequents with equal probability for each initial state).
  A dynamical system can have discrete or continuous time.
Notes: NEW

## Slide 42: DYNAMIC MODELS: definitions
Order of a dynamical system
  It is defined as the order of the dynamical mathematical model representing the system
Order of a single differential equation
  It is defined as the order of the highest derivative in the differential eq.
  Ex.: n-th order ODE:
Order of a system of differential equations
  It is defined as the sum of the orders of the individual differential eqs.
Notes: NEW

## Slide 43: MATHEMATICAL MODELS 1st CLASSIFICATION
  “First principle Models”
    Basic models
    Models involving transport phenomena
    Models based on the “population balance approach”
  Empirical or “fitting” models
  Dynamic models
    input-output dynamic models
    input-state-output dynamic models or state-space models
    dynamic black box models
  Time Series
  Statistical models
 rielaborated from § 1.4 in Himmelblau D.M. e Bischoff K.B., “Process Analysis and Simulation”, Wiley & Sons Inc., 1967
(on the base of the approach adopted for model development)

## Slide 44: DYNAMIC MODELS: input-output representation
MATHEMATICAL MODEL
Input output
 typical of automatic process control
 Stephanopoulos, §5.1
 Roffel & Betlem, 2006
 Giua & Seatzu, “Analisi dei sistemi dinamici”, 2006
An input-output equation reveals the direct relationship between the output variable desired, and the input variable.
This relationship often includes the derivatives of one or both variables.
Even with a higher order equation, the advantage is that the output variable is independent of (uncoupled from) any other variables except the inputs.
Notes: new

## Slide 45: INPUT-OUTPUT REPRESENTATION Variables
Basic Automatic Control prof. Guariso
Notes: new

## Slide 46: MATHEMATICAL MODELS 1st CLASSIFICATION
  “First principle Models”
    Basic models
    Models involving transport phenomena
    Models based on the “population balance approach”
  Empirical or “fitting” models
  Dynamic models
    input-output dynamic models
    input-state-output dynamic models or state-space models
    dynamic black box models
  Time Series
  Statistical models
 rielaborated from § 1.4 in Himmelblau D.M. e Bischoff K.B., “Process Analysis and Simulation”, Wiley & Sons Inc., 1967
(on the base of the approach adopted for model development)

## Slide 47: DYNAMIC MODELS: input-state-output representation
MATHEMATICAL MODEL
Input state output
 Giua & Seatzu, “Analisi dei sistemi dinamici”, 2006
     Behavioral models
     “internal” model of the process
     Roffel & Betlem, 2006
Intuitively, the state of a system describes enough about the system to determine its future behavior.

## Slide 48: Example 5 WATER OPEN TANK
h(t)
IN :
STATE: h(t)
OUT :
VARIABLES
Initial Condition: h(0) = h0
State equation:
Output transformation:
ACC = IN – OUT
 see also Ex. 6.1 pag. 118 and Ex. 6101 pag. 175 in Stephanopoulos
 An example of:
first principles model
input-state-output dynamic model

## Slide 49: INPUT-STATE-OUTPUT MODEL
Basic Automatic Control prof. Guariso
 Such a “memory”, required to define the present-time condition of the system, is called the state of the system at the time instant when the input is applied.
The variables x(t) defining the state are called state variables.
  The state of a dynamic system is such that the knowledge of the state variables at t = t0, together with the knowledge of the input variables for t  t0, completely determines the behavior of the system for any time t  t0.
Notes: Semplificare ed unificare

## Slide 50: STATE VARIABLES
Quantities describing the present state of a system enough well to determine its future behavior.
They provide a means to keep memory of the consequences of the past inputs to the system.
They may be partly coincident with output variables.
The minimum number of state variables required to represent a given system, n, is usually equal to the order of the system's defining differential equation.
The choices for variables to include in the state:
  is highly dependent on the fidelity of the model and the type of system
  is not unique
  as a HINT, the state variables are often given by the same variables appearing within the initial conditions of the system’s ODEs
Basic Automatic Control prof. Guariso
http://www.cds.caltech.edu/~murray/amwiki/index.php/FAQ:_What_is_a_state%3F_How_does_one_determine_what_is_a_state_and_what_is_not%3F
Notes: Semplificare ed unificare
Semplificare ed unificare

## Slide 51: STATE VARIABLES
Basic Automatic Control prof. Guariso
Notes: Semplificare ed unificare

## Slide 52: STATE-SPACE MODELS
Basic Automatic Control prof. Guariso
where:
The space spanned x(t) n is the state-space or phase-space
nN is the order or size of the model
The n components of x(t) are termed phases
The function f:+ ·n ·m →n is termed vector field

## Slide 53: LINEAR STATE-SPACE MODELS. Terminology
A is the state (or system) matrix [n·n]
B is the input matrix [n·m]
C is the output matrix [p·n]
D is the feedthrough matrix [p·m]
v is the time vector [n·1]
Initial Condition:
State equation:
Output
transformation:
A·x(t)
[n·n][n·1] = [n·1]
B·u(t)
[n·m][m·1] = [n·1]
v·t
[n·1][1·1] = [n·1]

## Slide 54: MATHEMATICAL MODELS 1st CLASSIFICATION
  “First principle Models”
    Basic models
    Models involving transport phenomena
    Models based on the “population balance approach”
  Empirical or “fitting” models
  Dynamic models
    input-output dynamic models
    state-space autonomous dynamic models
    dynamic black box models
  Time Series
  Statistical models
 rielaborated from § 1.4 in Himmelblau D.M. e Bischoff K.B., “Process Analysis and Simulation”, Wiley & Sons Inc., 1967
(on the base of the approach adopted for model development)

## Slide 55: AUTONOMOUS SYSTEM (definition based on the input-state-output representation)
A dynamical system is autonomous if the state is not depending on input
OR
the input is constant with time.
adapted from “notecontrolli_PRATTICHIZZO.pdf”
NB:
For a dynamic model described by a system of ODEs, an autonomous system is also time invariant
DYNAMICAL SYSTEM
Notes: NEW

## Slide 56: AUTONOMOUS SYSTEM (definition based on the shape of the vector field)
A dynamical system is autonomous if its vector field depends on the state x(t), but does not explicitly depend on time.
Examples of 2nd order systems:
Autonomous system Non-autonomous system
with x(t)n
t +
Notes: Da integrare con la prec.

## Slide 57: ORBITS OR TRAJECTORIES OF A DYNAMIC SYSTEM
The (forward) orbit or trajectory of a state variable x is the time-ordered collection of states that x follow from an initial state x0 using the system evolution rule (vector field).
When both state space and time are continuous, the forward orbit is a curve x(t) parametric in t≥0
Different initial states result in different trajectories
x1
x2
x0T = [x10, x20]
Example for a system of order n=2
Notes: NEW

## Slide 58: PHASE PORTRAIT
The set of all trajectories plotted in the state space forms the phase portrait of a dynamical system.
it is parametric in time
in practice, only representative trajectories are considered, indicating the forward time-orientation by an arrow
the phase portrait is usually built by numerical methods for nonlinear systems
The analysis of phase portraits provides an extremely useful way for visualizing and understanding qualitative features of solutions.
The phase portrait is particolarly useful for scalar (1st order) and planar systems (2nd order)
Example for a planar system
Notes: Cambiare il grafico

## Slide 59: TRANSIENTS AND REGIMES
The orbits may have a bounded or unbounded asymptotic behavior (for t  ± ).
If an orbit has a bounded asymptotic behavior for t  + , the part of the orbit describing such an asymptotic behavior is referred to as regime and the remaining part is referred to as transient.
The regimes (bounded) can be constant or dynamic
Notes: NEW

## Slide 60: CONSTANT REGIMES
The simplest and most well known constant regime (bounded) is the equilibrium point (steady-state point), which is possible for every system order n
x1
x2
x0T = [x10, x20]
Example for a system of order n=2
xsT = [x1s, x2s]
Notes: NEW

## Slide 61: EQUILIBRIUM POINT
Example for a 2nd order dynamical system:
Stable equilibrium point (STEADY STATE)
1D
2D
Time chart
or
Time trajectory
Orbit
Phase plane
Equilibrium point
Initial condition

## Slide 62: REGIMES
≥
≥
≥
≥
Notes: NEW

## Slide 63: PERIODIC REGIME
Example:
Stable LIMIT CYCLE for a 2nd order dynamical system
Limit cycle
Phase portrait
1D
2D
Time chart

## Slide 64: LIMIT CYCLE
Definition:
A closed asymptotic orbit in the phase space that results in a periodic oscillation of the state variables (phases), with amplitude and frequency depending on the properties of the non-linear dynamic system only and not on the chosen initial conditions.
 in order to have a Limit Cycle as an asymptotic orbit, the non-linear dynamic (continuous time) system must be of order 2 at least.
 the Limit Cycle cannot exist as an asymptotic orbit for linear dynamic system.
Notes: Trascrivere la nota !

## Slide 65: LIMIT CYCLE
n = 3
n = 2
Phase plane
Time chart
Examples:

## Slide 66: 2nd ORDER, NON-LINEAR, AUTONOMOUS SYSTEM
dx1/dt = f1(x1(t), x2(t))
dx2/dt = f2(x1(t), x2(t))
1st IC: x1(t0)=x10; x2(t0)=x20
2nd IC: x1(t0)=x11; x2(t0)=x21
Example of Phase Portrait
x1
x2
x0=[x10, x20]
x00=[x11, x21]

## Slide 67: THE DIABATIC CSTR Example No. 6
 Diabatic CSTR by Prof. B.W. Bequette:
http://www.rpi.edu/dept/chem-eng/WWW/faculty/bequette/education/links_mods/cstr/
An example of 2nd order, non-linear, autonomous system
Tj
Tf
control volume
T

## Slide 68: AUTONOMOUS SYSTEM (alternative formulation)
Notes: Immagine !

## Slide 69: SOLUTION OR BIFURCATION DIAGRAM
A solution diagram is a diagram in which the asymptotic regimes (at least the simplest of them) of a single state variable are reported as a function of a single model parameter.
Therefore this diagram allows to represent the possible regimes for each parameter value.
Furthermore, it also shows the (possible) bifurcation values of the parameter: in fact, they correspond to a change in type, number or stability of the asymptotic solutions.
Example of the 1st order system dx/dt = r x(t) - x (t)3
asymptotic
solution
model
parameter

## Slide 70: MATHEMATICAL MODELS 4th CLASSIFICATION
(based on the type of description adopted for time as the independent variable)
 VALID for DYNAMICAL SYSTEMS only
continuous time models
discrete time models

## Slide 71: CONTINUOUS-TIME SYSTEMS
The time changes continuously:
  it is not possible to define a minimum time interval
  it is always possible to consider a smaller time interval.
Accordingly, the theory of continuous-time systems has been defined and studied, where the variables of the system are continuous-time functions, that is, at every time instant t, it is possible to define and assign the variable value.
Continuous-time systems: t  ℜ

## Slide 72: DISCRETE-TIME SYSTEMS
Ingresso uscita
Input output
input – output representation
MATHEMATICAL MODEL
input – state – output representation
MATHEMATICAL MODEL
Ingresso stato uscita
Input state output

## Slide 73: INPUT–STATE–OUTPUT DISCRETE-TIME SYSTEMS General representation of models
EXPLICIT TYPE
“IMPLICIT” TYPE
SCALAR SYSTEMS: x(k) is a scalar variable
VECTOR SYSTEMS: x(k) is a vectorial variable of size n
   A deterministic system with discrete time is often defined a map.
State equation
Output transformation
State equation
Output transformation

## Slide 74: MODEL ORDER
The order n is an integer number obtained as the product between the size of the space vector x and the time gap in the implicit model representation.
 The time gap is the max time distance in the implicit model representation
Example 1:
autonomous discrete-time model of order 1 (scalar model)
Example 2:
autonomous discrete-time model of order 2 (vectorial model)

## Slide 75: FIXED POINT
DEFINITION of a fixed point:
x(k+1) = x(k)
x(k) may be a scalar or vector variable
A fixed point can be stable or unstable.
A stable fixed point is an attractor for the trajectories originating in a reasonable neighborhood of it.
AUTONOMOUS SYSTEMS
The fixed points are determined for autonomous systems x(k+1) = f(x(k)) as the solutions of the algebraic eq. (scalar) or system of eqns. (vector):
x*= f (x*)

## Slide 76: PERIODIC REGIMES
x(k+1) = f (x(k))
x(k+j)=x(k)
x(k+q)≠x(k)
with q  N and q < j
periodical regimes with period “j”
in an autonomous discrete-time model
x(k) =x(k+1) = f (x(k))
 The fixed point can be viewed as a periodical regime with period “1”
k0 … … … k k+1 … k+q … k+j … … … k+2j …

## Slide 77: ORBITS OR TRAJECTORIES
Example:
discrete-time, non-linear, autonomous model of order 2
fixed point
periodic regime
Phase Portrait

## Slide 78: LOGISTIC MODEL
a natural saturation level Nsat exists for the population at which the growth rate becomes zero
Search for Equilibrium Points

## Slide 79: LOGISTIC MAP
adimen-
siona-lization
discreti-zation

## Slide 80: LOGISTIC MAP WITH 1 PARAMETER
x(k+1) = r [1 - x(k)] x(k)
x(k0) = x0
0 ≤ x(k) ≤ 1
x(k+1)→y x(k)→x
Parabola that is
passing through the origin
having a vertical axis
having a downward concavity
having vertex coordinates: (-b/2a; -Δ/4a)
Diagram of Generalized Eq. y = f(x)
r = growth rate parameter

## Slide 81: LOGISTIC MAP: Analytical determination of fixed points
81
x* = r x* (1 - x*)
 
1st solution 2nd solution
x* = 0 x* ≠ 0
1 = r (1 - x*)
x* = 1 – 1/r
 x* only for r>1
Notes: 81

## Slide 82: LOGISTIC MAP: Graphical determination of fixed points Example
82
x(k+1)
x(k)
fixed points x*= f (x*) by intersection
Logistic map.: x(k+1)=3.55 x(k)(1-x(k))
Bisector of 1st quadrant: x(k+1) = x(k) locus of fixed points
← vertex r/4
Notes: 82

## Slide 83: COBWEB or STAIRCASE CONSTRUCTION Example
From Wikipedia, the free encyclopedia: http://en.wikipedia.org/wiki/Cobweb_plot
logistic map: x(k+1)= r x(k)(1-x(k))
bisector of 1st quadrant: x(k+1) = x(k)
initial condition: x0 = 0.08
r ≈ 2.6 (estimated)
← vertex r/4

## Slide 84: THE LOGISTIC MAP IN MATLAB
84
Useful scripts:
cobweb.m
logistic_time_trajectory.m
logistic_solution_diagram.m
r=0.75;
r=1.5;
r=2.5;
r=3.2;
r=3.5;
r=3.55;
r=3.8;
r=3.83;
r=3.9
 try the script cobweb.m
with the following values for r:
Notes: 84
riferimento

## Slide 85: LOGISTIC MAP
r=0.75 x0=0.5
Cobweb
stable fixed point: x* = 0 (“trivial solution”)
← vertex r/4

## Slide 86: LOGISTIC MAP
r=1.5 x0=0.05
Cobweb
stable fixed point x* = (1 – 1/r)
← vertex r/4

## Slide 87: LOGISTIC MAP
r=2.5 x0=0.05
Cobweb
stable fixed point x* = (1 – 1/r)
← vertex r/4

## Slide 88: LOGISTIC MAP
Time Trajectories for r = 2.5
x0=0.05 (in blu)
x0=0.06 (in red)

## Slide 89: LOGISTIC MAP
r=3.2 x0=0.05
Cobweb
Time Trajectory
unstable fixed point x* = (1 – 1/r)
period 2 dynamic regime: x= 0.513, 0.799
← vertex r/4

## Slide 90: LOGISTIC MAP
r=3.5 x0=0.05
Cobweb
Time Trajectory
← vertex r/4
unstable fixed point x* = (1 – 1/r)
period 4 dynamic regime

## Slide 91: LOGISTIC MAP
r=3.55 x0=0.36
Cobweb
Time Trajectory
← vertex r/4
unstable fixed point x* = (1 – 1/r)
period 8 dynamic regime

## Slide 92: LOGISTIC MAP: switch to deterministic chaos
92
Cobweb: x0=0.05 100 steps
Cobweb: x0=0.05 100 steps
r=3.569945673
r=3.569945671

## Slide 93: LOGISTIC MAP
r=3.8 x0=0.17
Cobweb
chaotic solution (aperiodic dynamic regime)
Time Trajectory
← vertex r/4

## Slide 94: LOGISTIC MAP: Deterministic caos
Time Trajectories for r=3.8:
x0=0.17 (in blu)
x0=0.18 (in red)
 sensible dependence from initial conditions

## Slide 95: LOGISTIC MAP
r=3.83 x0=0.33
Cobweb
period 3 dynamic regime
← vertex r/4

## Slide 96: LOGISTIC MAP
period 3
x0=0.95
Time Trajectories
r=3.83
x0=0.33

## Slide 97: LOGISTIC MAP
r=3.9 x0=0.05
Cobweb
aperiodic regime
Time Trajectory
← vertex r/4

## Slide 98: LOGISTIC MAP
Cobweb
x0=0.2
r =1  4
From Wikipedia, the free encyclopedia: http://en.wikipedia.org/wiki/File:LogisticCobwebChaos.gif
Notes: 98

## Slide 99: LOGISTIC MAP: remarks on Fixed points
for 0 < r < 1 one fixed point x*=0 exists, i.e., the origin, and is stable
for 1 < r < 3 two fixed points exist: one is unstable (x*=0) and the other one x*=(r-1)/r is stable
for r > 3 the fixed point becomes unstable, but a new stable periodic regime arises with a period 2k and k ε N (period doubling cascade)
the periodic regime holds up to a particular value rc, = 3.569945672.., beyond which the map seems to oscillate among an infinite number of points without any regular law:  deterministic chaos
for certain values rc < r < 4 there are still periodic windows

a stable fixed point is referred to as attractor
a stable periodic regime is referred to as periodic attractor

## Slide 100: LOGISTIC MAP. Solution diagram
100
x0=0.05
x0=0.3

## Slide 101: LOGISTIC MAP: regime patterns
The table shows the type of cycles that can be observed and the value of the growth parameter r for which that cycle appears:
Notice that the period doubling happens faster and faster (8, 16, 32, ...) and then suddenly ends after the so-called accumulation point and chaos appears.
If we call rn+1 the value of r for which the 2n period becomes unstable and if we determine the limit, as n goes to infinity, of ( rn+1 - rn ) / ( rn+2 - rn+1 ) we obtain a value of 4.66920160...
Surprisingly, that limit value is the same for all functions of this type ( 1D maps with only one quadratic maximum) which approach chaos by period doubling.
In fact, that value is one of the universal constants - the Feigenbaum constant - approximately equal to 4.669. It was discovered by Feigenbaum in 1975 and it characterizes the transition to chaos.
n | 2n | rn
1 | 2 | 3
2 | 4 | 3.449490
3 | 8 | 3.544090
4 | 16 | 3.564407
5 | 32 | 3.568750
6 | 64 | 3.56969
7 | 128 | 3.56989
8 | 256 | 3.569934
9 | 512 | 3.569943
10 | 1024 | 3.5699451
11 | 2048 | 3.569945557
infinity | accumulation point | 3.569945672
from http://to-campos.planetaclix.pt/fractal/caose.html

## Slide 102
  Modelli a “principi primi” (“First principle Models”)
  Modelli basati sul “bilancio di popolazione”
  Modelli empirici o di “fitting”
  Dynamic models
    input-output dynamic models
    input-state-output dynamic models or state-space models
    dynamic black box models
  Serie temporali
  Modelli statistici
MATHEMATICAL MODELS 1st CLASSIFICATION
(on the base of the approach adopted for model development)

## Slide 103: Black-Box Model Structures
The model structures vary in complexity and order depending on the flexibility you need to account for the dynamics and on possible consideration of noise in your system.
The simplest black-box structures are:
Linear polynomial model, which is the simplest input-output model (e.g., ARX model)
Transfer function, with a given number of adjustable poles and zeroes.
State-space model, with unknown system matrices, which you can estimate by specifying the number of model states
Non-linear parameterized functions
103
u(t) OR u(k) y(t) OR y(k)
Input Output
BLACK BOX
MODEL
Notes: Vero ANCHE tempo continuo?
103

## Slide 104: SYSTEM IDENTIFICATION
System identification is a methodology for building mathematical models of dynamic systems using measurements of the system's input and output signals/data.
The system identification methodology requires that you:
Measure the input and output signals/data from your system in time or frequency domain.
Select a model structure.
Apply an estimation method to estimate value for the adjustable parameters in the candidate model structure.
Evaluate the estimated model to see if the model is adequate for your application needs.
System identification uses the input and output signals you measure from a system to estimate the values of adjustable parameters in a given model structure.
Obtaining a good model of your system depends on how well your measured data reflect the behavior of the system.
Documentation center

## Slide 105: Dynamical modeling Final Statement
105
A way to distinguish the techniques used when modeling dynamic processes is to picture them on a scale with two extremes at the ends:
at the one side black box system identification
at the other side theoretical modeling or first principles modeling
Notes: 105

## Slide 106: MATHEMATICAL MODELS 5th CLASSIFICATION
  1. ANALYTICAL SOLUTIONS  DIFFERENTIAL CALCULUS
       ALGEBRA
2. NUMERICAL SOLUTIONS  NUMERICAL CALCULUS
      Ex.: numerical methods for PDEs
  FINITE DIFFERENCE METHODS (FDM)
  FINITE ELEMENT METHODS (FEM)
  COLLOCATION METHODS
(based on the type of mathematical solution,
with exclusion of empirical models)

## Slide 107
  Modelli a “principi primi” (“First principle Models”)
  Modelli basati sul “bilancio di popolazione”
  Modelli empirici o di “fitting”
  Modelli dinamici
    Modelli dinamici “con rappresentazione ingresso-uscita”
    Modelli dinamici “con rappresentazione nello spazio di stato”
    Modelli dinamici a scatola nera (black box)
  Time Series
  Modelli statistici
MATHEMATICAL MODELS 1st CLASSIFICATION
(on the base of the approach adopted for model development)

## Slide 108: TIME SERIES: Definitions
A time series is a sequence of data points, measured typically at successive times spaced at uniform time intervals.
Y1, Y2,…, a series of values measured or observed for a variable Y at successive times t1, t2,… which may be reported as a sequence of integers k = 0, 1, 2, . . .
Anonymous
Values taken by a variable over time (such as daily sales revenue, weekly orders, monthly overheads, yearly income) and tabulated or plotted as chronologically ordered numbers or data points.
http://www.businessdictionary.com/
 time series are NOT just data …

## Slide 109: TIME SERIES: Examples
the daily closing value of the Dow Jones index
the annual flow volume of the Nile River at Aswan
the sampled pressure measurements in a gas-phase chemical reactor
. . .
the retail garment market sellings