## Slide 1: NOTES ON STABILITY FOR NON-LINEAR SYSTEMS
Michele MICCIO
and Andrea CAMMAROTA
Rev. 3.8 of May 23, 2019
Dept. of Industrial Engineering (Università di Salerno)
Prodal Scarl (Fisciano)

## Slide 2: Different behaviors between linear and nonlinear systems
There are phenomena that can take place only in the presence of nonlinearity in the dynamical model; hence they cannot be described or predicted by linear models.
The following are examples of nonlinear phenomena:
Finite escape time: The state of an unstable linear system can go to infinity as time approaches infinity. A nonlinear system’s state, however, can go to infinity in finite time.
Multiple isolated equilibrium points: A linear system can have only one equilibrium point, and thus only one steady-state operating point that attracts or repels the state of the system irrespective of the initial state. A nonlinear system can have more than one equilibrium point.
Limit cycles: A linear system can have a stable oscillation if it has a pair of eigenvalues on the imaginary axis. The amplitude of the oscillation will then depend on the initial conditions. A nonlinear system can exhibit an oscillation of fixed amplitude and frequency, which appears independently of the initial conditions.
Chaos: A nonlinear system can have a more complicated steady-state behavior that is not equilibrium or periodic oscillation. Some of these chaotic motions exhibit randomness, despite the deterministic nature of the system.
Multiple modes of behavior: A nonlinear system may exhibit very different forms of behavior depending on external parameter val- ues, or may jump from one form of behaviour to another autonomously. These behaviors cannot be observed in linear systems, where the complete system behaviour is characterized by the eigenvalues of the system matrix A.
 NLSC_lecture_notes_2017 (ETH, P. Al Hokayem & E. Gallestey)

## Slide 3: Introduction
QUESTIONS
How many steady-state regimes does a dynamical system have?
What are the stability properties of a given steady-state regime?
For clarity and simplicity, we concentrate on stability of
 constant regimes (equilibrium points in the continuous time domain)
http://www.scholarpedia.org/article/Equilibria

## Slide 4: Constant Regimes: How many ?
Multiplicity of Equilibrium Points

## Slide 5: What are the stability properties ? A qualitative concept
An equilibrium may be stable or unstable or indifferent. For example:
the equilibrium of a pencil standing on its tip is unstable;
the equilibrium of a picture on the wall is (usually) stable;
the equilibrium of a ball on a flat plane is (usually) indifferent.
Adapted from On-Line Lectures ©Alexei Sharov, Department of Entomology, Virginia Tech, Blacksburg, VA
http://www.ento.vt.edu/~sharov/PopEcol/

## Slide 6: What are the stability properties ? A qualitative concept (2)
The concept of stability can be illustrated by a cone placed on a plane horizontal surface.

## Slide 7: Stability: general properties
Linear Systems | Non-Linear Systems
stability is an intrinsic property of the system itself and not of its equilibrium points | stability is a property of each asymptotic regime and not of the system itself; e.g., the same dynamic system may exhibit stable and unstable equilibrium points in parallel

## Slide 8: Stability for INPUT-OUTPUT DYNAMICAL systems

## Slide 9: Stability for linear input-output systems
A necessary and sufficient condition for a linear dynamic system to be stable is that all the poles of the system transfer function have negative real parts (BIBO Stability Theorem).
A marginally stable input-output system has only certain bounded inputs resulting in a bounded output.
http://en.wikipedia.org/wiki/Marginal_stability
 Part IB Paper 6: Information Engineering from Glenn Vinnicombe

## Slide 10: Stability for AUTONOMOUS DYNAMICAL systems

## Slide 11: Lyapunov Stability definition (for a point of equilibrium xs)
A point of equilibrium xs of the above system is said to be Lyapunov stable if, for every region U of radius  >0, there exists a neighborhood V of radius  > 0 such that, for each initial condition x0V, the corresponding trajectory x(t) remains included in U for every t>t0
that is:
Conceptually, the meaning is the following:
Trajectories (e.g., perturbations from equilibrium) starting "close enough" to xs (within a distance δ from it) remain "close enough" forever (within a distance  from it). Note that this must be true for any  that one may want to choose, otherwise the system is unstable!
e
d
x0
xs
x(t)
Consider an autonomous nonlinear dynamical system
Notes: v. Formalismo matem. Di M.T. D’Agosto

## Slide 12: Lyapunov Asymptotic Stability definition (for a point of equilibrium xs)
A point of equilibrium xs of the above system is said to be asymptotically stable if it is Lyapunov stable and if a neighborhood V of radius  > 0 exists such that, for each initial condition x0V and for t  
Conceptually, the meaning is the following:
Trajectories (e.g., perturbations from equilibrium) that start "close enough" to xs (within a distance δ from it) not only remain close enough, but also eventually converge to the equilibrium.
Consider the same autonomous nonlinear dynamical system
e
d
x0
xs
x(t)
1st example 2nd example
Notes: v. Formalismo matem. Di M.T. D’Agosto

## Slide 13: Instability
A point of equilibrium xs is said to be unstable if it is not Lyapunov stable
http://www.scholarpedia.org/article/Stability

## Slide 14: Example: 2nd order dynamical system
 retrieved from Dr. Victor M. Becerra, University of Reading (UK)
phase portrait
 The origin is an equilibrium point

## Slide 15: Qualitative concept of stability vs. Lyapunov Stability
 Adapted from Economia dei Sistemi Complessi dei proff.ri Silvio Giove e Christina Mosele
stable equilibrium | unstable equilibrium | indifferent or neutral equilibrium
Lyapunov’s Asymptotic Stability | Lyapunov Instability | Lyapunov Stability

## Slide 16: Linear autonomous dynamical systems

## Slide 17: Study of linear autonomous dynamical systems
n-ORDER, LINEAR AUTONOMOUS DYNAMICAL SYSTEM
x is state:
A is a non singular state matrix [n · n]
If A is non singular , x = 0 is the only steady state.
EQUILIBRIUM POINTS
… understanding linear systems and their solutions is a crucial first step to understanding the more complex nonlinear systems.
For this part see ch. 27 of:
 D.R. Coughanowr, L.B. Koppel, Process systems analysis and control
UniSA library 660.281 5 COU

## Slide 18: Linear autonomous dynamical systems: definitions
EIGENVALUES and EIGENVECTORS
The eigenvectors v of a square matrix are the non-zero vectors which, after being multiplied by the matrix, remain proportional each one to the original vector (i.e., change only in magnitude, not in direction).
For each eigenvector, the corresponding eigenvalue λ is the factor by which the eigenvector magnitude changes when multiplied by the matrix.
EIGENVALUES
Solutions of the eq.:

## Slide 19: Linear autonomous dynamical systems: definitions
HYPERBOLICITY
A linear autonomous dynamical system is said to be hyperbolic if all eigenvalues have nonzero real part.
A linear autonomous dynamical system is said to be non-hyperbolic if at least one eigenvalue has a real part equal to zero.
ORBITS
Assumptions:
1) n distinct Eigenvalues and Eigenvectors, (i.e., each eigenvalue λi has a unit algebraic multiplicity)
2) at least i is complex
INVARIANT
A subset A of the state space X is said to be invariant if the orbits starting at each of its points (x0A) are totally included in A (x(t)A).
If an eigenvalue λi has a unit algebraic multiplicity, the corresponding (real) eigenvector vi forms a uni-dimensional invariant subspace (autospace of the matrix A relative to the eigenvalue λi).
Notes: "invariant". Se v è reale e la condizione iniziale appartiene alla retta passante per l’origine e parallela a v, l’evoluzione del sistema è contenuta in tale retta per ogni t. A causa di tale comportamento le direzioni individuate dagli autovettori reali (autospazi) si dicono invarianti. La stabilità su tali rette può essere determinata con le regole date per i sistemi lineari del primo ordine.

## Slide 20: Linear autonomous dynamical systems: Stability
SYSTEM STABILITY
Asymptotically Stable if Re(i)<0  i
Unstable if at least one eigenvalue i exists with a positive real part
ORBITS
x(t) is bounded if the terms
do not diverge.
Therefore:

## Slide 21: Autonomous dynamical systems: an example in the planar case
order n = 2
phase portrait
orbit
or
trajectory

## Slide 22: Linear autonomous dynamical systems: the planar case
Assumptions:
A is invertible,
The eigenvalues 1 and 2 are non-zero.
v1 and v2 are the corresponding eigenvectors
c1 and c2 are constants
The origin (0,0) is the only steady-state point
The general solution is:

## Slide 23: Planar linear dynamical systems: the hyperbolic case
2)
1)
3)
1bis)
2bis)
Real Complex and conjugate

## Slide 24
Planar linear dynamical systems: the non-hyperbolic case
4)
5)
6)
8)
7)
With 2 indipendent eigenvectors
With only 1 indipendent eigenvector
Real Imaginary and conjugate

## Slide 25: PPlane
MATLAB and JAVA software for simulation and stability analysis of 2nd order (planar) systems, either linear or non-linear
http://math.rice.edu/~dfield/

## Slide 26: Phase Portrait: 1) 1 and 2 are real, distinct and negative
Eigenvalues 1= -1 2= -4
(NODO STABILE)
Knot or Nodal Sink
Eigenvectors
(coincident with axis versors)

## Slide 27: Phase Portrait: 1) 1 and 2 are real, distinct and negative
Eigenvalues 1= -1 2= -4
(NODO STABILE)
Knot or Nodal Sink
Eigenvectors (not orthogonal !)
invariant

## Slide 28: Phase Portrait: 2) 1 and 2 are real, distinct and positive
Eigenvalues 1=4 2=1
(NODO INSTABILE)
Unstable Knot or Nodal Source
Eigenvectors (not orthogonal !)

## Slide 29: Phase Portrait: 3) 1 and 2 are real, distinct and opposite
Eigenvalues 1= -1 2= 3
(SELLA)
Saddle
Eigenvectors (not orthogonal !)
invariant

## Slide 30: Phase Portrait: 1bis) 1 and 2 complex with a negative real part
Eigenvalues 1= -1+3j 2= -1-3j
Eigenvectors
(complex !)
(FUOCO STABILE o POZZO A SPIRALE)
Stable Focus or Spiral Sink

## Slide 31: Phase Portrait: 2bis) 1 and 2 complex with a positive real part
Eigenvalues 1=1-2j 2=1+2j
Eigenvectors
(complex !)
(FUOCO INSTABILE)
Spiral Source

## Slide 32: Phase Portrait: 8) 1 and 2 imaginary (non hyperbolic)

The amplitude of the oscillation will depend on the initial condition.
NOT an asymptotically stable equil. point !
Eigenvalues 1= -2j 2= 2j
Eigenvectors
(complex !)
(CENTRO)
Center

## Slide 33: Planar linear dynamical systems: Eigenvalues

## Slide 34: Planar linear dynamical systems: real and distinct Eigenvalues
The eigenvalues are real and distinct when the discriminant Δ is positive
The sign of eigenvalues is from Carthesius rule:
Possible Cases |  | 
Unstable Knot | 1,2R 1>0, 2>0 | Det(A)<[Tr(A)]2/4 Tr(A)>0 Det(A)>0
Stable Knot | 1,2R 1<0, 2<0 | Det(A)<[Tr(A)]2/4 Tr(A)<0 Det(A)>0
Saddle | 1,2R 1<0, 2>0 | Det(A)<[Tr(A)]2/4 Det(A)<0 Tr(A)− 0  there are always a variation and a permanence in sign, whatever Tr(A)=0  there are two eigenvalues, real and opposed in sign

## Slide 35: Planar linear dynamical systems: real and coincident Eigenvalues
The eigenvalues are real and coincident when the discriminant Δ is null
This can be viewed as the eq. for a parabola passing through the origin, having its vertical axis (Det A) coincident with the y-axis
Possible Cases |  | 
Unstable Knot | 1,2R 1 = 2 = Tr(A)/2 > 0 | Det(A) = [Tr(A)]2/4 Tr(A)>0
Stable Knot | 1,2R 1 = 2 = Tr(A)/2 < 0 | Det(A) = [Tr(A)]2/4 Tr(A)<0

## Slide 36: Planar linear dynamical systems: complex and coniugate Eigenvalues
Possible Cases |  | 
Unstable Focus | 1,2C-R Re(1)=Re(2)>0 | Det(A)>[Tr(A)]2/4 Tr(A)>0
Stable Focus | 1,2C-R Re(1)=Re(2)<0 | Det(A)>[Tr(A)]2/4 Tr(A)<0
Center | 1,2C-R Re(1)=Re(2)=0 | Det(A)>[Tr(A)]2/4 Tr(A) = 0
The eigenvalues are complex and coniugate when the discriminant Δ is negative

## Slide 37: Planar linear dynamical systems: General Diagram
Tr(A)
det(A)

## Slide 38: Planar linear dynamical systems: attractors and repellors
n = 2
eigenvalues

## Slide 39: Non-linear autonomous dynamical systems

## Slide 40: Linearization around a steady-state point
Let xs be a steady-state point, which can be stable or unstable.
Let’s use Taylor expansion:
f(x)= f(xs)+ J(xs) (x- xs)+ O(| x- xs|2)
f(xs) = 0 as it’s a steady-state;
The linear term is the product between the Jacobian matrix J and the vector (x – xs).
The term O(| x- xs|2) is an infinitesimal of order of | x- xs|2 and is negligible when x→ xs.
Notes: MANCA Taylor !

## Slide 41: Stability of non-linear systems: Linearization Method
The non-linear system is linearized with a 1st order Taylor expansion around xs;
y(t) = x(t) - xs is set (deviation variables)
the new linearized system is analized according to the theory of stability for linear systems
dy/dt = J(xs) y(t)
Lyapunov Theorem
(Lyapunov's indirect method)
If the new linearized system has all eigenvalues with a negative real part (asymptotically stable steady-state) then the steady-state is asymptotically stable even for the original non linear system
If the new linearized system has at least one eigenvalue with a positive real part (unstable steady-state) then the steady-state is unstable even for the original non linear system
Nothing can be concluded in other cases

## Slide 42: Summary
1. Linearizazion Method (Lyapunov's indirect method)
2. Lyapunov's 2nd method for stability (1892)
is more general
makes use of a Lyapunov function V(x) which has an analogy to the potential function of classical dynamics.
3. Direct Simulation Methods

## Slide 43: The diabatic CSTR as the prototype of non-linear autonomous dynamical systems

## Slide 44: THE DIABATIC CSTR Example No. 6
 Diabatic CSTR by Prof. B.W. Bequette:
http://www.rpi.edu/dept/chem-eng/WWW/faculty/bequette/education/links_mods/cstr/
An example of 2nd order, non-linear, autonomous system
Tj
Tf
control volume
T

## Slide 45: THE DIABATIC CSTR Example No. 6
 Diabatic CSTR by Prof. B.W. Bequette:
http://www.rpi.edu/dept/chem-eng/WWW/faculty/bequette/education/links_mods/cstr/
Mass balance on A species
Energy balance balance
Overall mass balance

## Slide 46: THE DIABATIC CSTR Example No. 6
 Diabatic CSTR by Prof. B.W. Bequette:
http://www.rpi.edu/dept/chem-eng/WWW/faculty/bequette/education/links_mods/cstr/
Classifications
“first principles” math model (1st classification)
structured model (2nd classification)
non-linear because of Arrhenius (3rd classification)
continuous time (4th classification)
2nd order
autonomous
state variables CA, T  x = (CA T)T
IC: x0 = (CA0 T0)T

## Slide 47: The Diabatic CSTR: a Matlab code
Reference:
https://it.mathworks.com/matlabcentral/fileexchange/13556-continuously-stirred-tank-reactor-cstr
% CSTR model from Michael A. Henson and Dale E. Seborg. Nonlinear Process Control.
% Prentice Hall PTR, Upper Saddle River, New Jersey, 1997.
% Description:
% Continuously Stirred Tank Reactor with energy balance and reaction A->B.
% The temperature of the cooling jacket Tc is the input variable.
% The concentration of A and temperature are the state variables.
% The code calculates and plots the Time Chart.

## Slide 48: The Diabatic CSTR: multiple steady-states from the entalpy balance
Van Herden stability analysis:
arbitrarily extends the steady-state entalpy balance to unsteady conditions;
is effective in determining unstable regimes, but not the stable ones.
QR
QE
case C)
Reference:
[1] Multiple Steady States in a Continuously Stirred Tank Reactor. http://www.rpi.edu/dept/chem-eng/WWW/faculty/bequette/education/links_mods/cstr/
Van Herden stability analysis
The energy removal rate is linear and has two terms (1) the energy needed to change the feed temperature to the reactor temperature, and (2) the energy removed or added by heat transfer to a cooling/heating fluid, which is at a constant temperature.
At steady state:

## Slide 49: The Diabatic CSTR: multiple steady-states from the mass balance
Reference:
See Ch. 8 in Levenspiel O., Chemical Reaction Engineering, 1972
Van Herden stability analysis
The non-dimensional conversion has two terms (1) from the energy balance (EB), and (2) from the mass balance (MB)
At steady state:
XA,EB = XA,MB
case C)

## Slide 50: The Diabatic CSTR: multiple steady-states from the mass balance
Reference:
http://demonstrations.wolfram.com/MultipleSteadyStatesInAContinuouslyStirredTankReactor/
www.colorado.edu/learncheme/kinetics/MultipleSteadyStatesCSTRnoHeat.html

## Slide 51: The Diabatic CSTR: non-dimensional model
Non-dimensional variables:
                t’=t/tR
Non-dimensional parameters:
Model:
Notes: Da e Beta da verif.

## Slide 52: Diabatic CSTR: multiple steady-state (Da=0.04; beta=1.5)
phase portrait
Notes: Introdurre I par. Adimensionali
Ed adim. Le eq. !!!

## Slide 53: Diabatic CSTR: stable steady-states
low conversion
high conversion
Stable Knot
Coordinates (0.043,0.388)
Eigenvalues -1.14, -1.48
Eigenvectors
(0.400, -0.916)
(-0.09, 0.995)
Stable Focus
Coordinates (0.921, 8.11)
Eigenvalues -2.14+4.01j
-2.14-4.01j
Eigenvectors
(0.041+0.016j, -0.999)
0.041-0.016j, -0.999)

## Slide 54: Diabatic CSTR: unstable steady-state
Saddle
Coordinates (0.412,3.64)
Eigenvalues -0.751, 3.23
Corresponding Eigenvectors: (-0.304, -0.952)
(-0.061, 0.998)
phase portrait
nullcline

## Slide 55: Diabatic CSTR: dynamical (periodic) regime (Da=0.07; beta=2.3)
phase portrait
Stable limit cycle
unstable steady-state

## Slide 56: Diabatic CSTR: limit cycle (Da=0.07; beta=2.3)
t’
time trajectories (corresponding)
phase portrait

## Slide 57: Diabatic CSTR
the solution diagram

## Slide 58: Concept of bifurcation
A nonlinear dynamic system differs from a linear dynamic system in that its qualitative properties can change under small perturbations of the model parameters.
These properties include the number of equilibria, stability of the equilibria, existence of limit cycles, multiple modes of behavior, and chaos.
 Zhang, Y. and Henson, M. A. (2001), “Bifurcation analysis of continuous biochemical reactor models”, Biotechnology Progress, 17, p. 647-660
Bifurcation is a sudden and drastic change in important properties of a nonlinear system (e.g., type of asymptotic regimes or their stability), following a smooth gradual change in one or more model parameters (“bifurcation parameters”) deviating from their design or predetermined values.
 Cosenza and Miccio (2015)
Notes: In generale, si dice che un parametro attraversa un valore di biforcazione quando determina il passaggio fra due situazioni dinamiche qualitativamente diverse, dovuto ad esempio alla creazione o scomparsa di punti di equilibrio o altri tipi di regimi asintotici, oppure cambiamenti di stabilità.
Gian-Italo Bischi, Rosa Carini, Laura Gardini e Paolo Tenti pubblicato sul n. 47 di Lettera matematica pristem