## Last name NOVELLO Name Ottavio student ID No.:
PC No. ___________

# Section 4: STABILITY OF LINEAR DYNAMIC SYSTEMS
A dynamic process Gp(s) has the following transfer function

G_p =1 over n left ( {-{n - 0.25} over {n + 0.25}} right )^n over left ( {{n s}^2 + 1 over n} right )

where n = PC No.24

Is this a rational transfer function?
Yes it is:
>> Gp=(1/n)*((-n-0.25)/(n+0.25))^n/(n*s^2+(1/n))

Transfer function:
    0.04167
----------------
24 s^2 + 0.04167

How much is type “g”?
proper function

How much is the gain?

dcgain--> Kc=dcgain(Gp)

Kp =

     1

How many and how much are the time constants?

The factorized function is:
Zero/pole/gain:
   0.0017361
----------------
(s^2 + 0.001736)

at denominator we have a second order system, whose general structure is:

tau^2*s^2+2*z*tau*s+1

where: z=damping factor=0
tau=time constant

In this case I can find tau in the following way:

  >> tau=sqrt(1/0.001736)

tau =

   24.0008

Because it is a second order system, there are two time constants that are real and coincident:
tau1=tau2=24.00 min
## Part A: Root locus
For the system Gp(s):

Plot the root locus by means of Matlab and SisoTool resources and attach it here

Is it a direct or inverse root locus?

Zero/pole/gain:
   0.0017361
----------------
(s^2 + 0.001736)

K=0.0017361 → K>0
Because the transfer constant (K) is larger than zero, it is a direct root locus

Provide a short comment to the trajectories
The poles and zeroes of the system are:
p=pole(Gp)

p =

        0 + 0.0417i
        0 – 0.0417i

and

 z=zero(Gp)

z =

   Empty matrix: 0-by-1

there are no zeroes and poles situated on Imaginary axes. So the trajectories are coincident with imaginary axes and they are going to +infinity,
respectively from: p1= 0 + 0.0417i and p2= 0 -0.0417i.
This happens because there are no zeroes where trajectories can end.
## Part B: Frequency response
For the dynamic system Gp(s) and a P controller with Kc=1:

Plot the Bode Diagrams by means of Matlab resources, with a log scale of the magnitude (NOT in dB), and attach them here

Does a resonance frequency exist? How much is it?
The resonance frequency exists if the AR curve shows a maximum peak over the value of AR=1. As it can be observed in the figure, the resonance frequency exists in this case.
W=0.0417 rad/s

It can also be calculated through:

zita=0
w0=1/tau*sqrt(1-2*zita^0)
w0 =

    0.0417

Decide if the Bode stability criterion is applicable

The bode stability criterion is applicable

If yes, is the above system closed-loop stable?

Yes, the system is closed loop stable.

Plot and attach here the extended Nyquist diagram together with the unit circle by means of Matlab resources, then discuss it in details

Nyquist plot
Check, on the base of the Nyquist stability criterion, if the above system is closed-loop stable

Sistema asintoticamente stabile se e solo se
Il diagramma non intercetta il punto critico(-1,0) (se lo interseca si dice che il sistema è in condizioni di stabilità marginale).

Il diagramma completo di Nyquist compie attorno al punto critico (-1,0) tanti giri in senso antiorario quanti sono i poli a parte reale positiva .

Compie tanti mezzi giri in senso antiorario (anche senza circondare il punto critic) quanti sono i poli immaginari puri.

Il 3 punto n on è rispettato--> il sistema non è asintoticamente stabile per nyquist
## Part C: Dynamic responses in the time domain
Take the following three dynamic systems, all in series in the control loop:
a P controller, with a convenient value of Kc according to your best judgement,
the above dynamic system Gp(s),
a measuring system Gm(s):
G_m =left ( {-1} right )^{n + 1} over {s + left ( {n - 0.25} over {n + 0.25} right )}

where n = 24
>> Gm=(-1)^(n+1)/(s+(n-0.5)/(n+0.5))

Transfer function:
    -1
----------
s + 0.9592

>>Gp

Transfer function:
    0.04167
----------------
24 s^2 + 0.04167

Gpp=Kc

Impongo Kc=1

Gpp=1

>> Gp2=Gp*Gm*Gpp

Transfer function:
        -0.04167
----------------------------------------
24 s^3 + 23.02 s^2 + 0.04167 s + 0.03997

Then, use the Matlab resources to:

plot the open-loop dynamic response to a unit step, attach it here

plot the open-loop dynamic response to impulse, attach it here and compare to unit step

Oscillating pattern for both!.

plot the closed-loop dynamic response to a unit step in the set point, attach it here and give your comments

plot the closed-loop dynamic response to a unit step in the disturbance, attach it here and give your comments

exactly the same pattern !