## Slide 1: TSPC_Exam_2015-11-06 Nyquist diagram Matlab construction with tricks, doubts and alternatives
Solution with n = 22
Rev. June 10, 2022 by M. Miccio

## Slide 2: TSPC_Exam_2015-11-06 Nyquist by default
n = 22
As plotted by the command nyquist at the prompt


## Slide 3: TSPC_Exam_2015-11-06 extended Nyquist zoomed
🤔
Straight lines drawn by Matlab to connect the Nyquist points at infinity.
 They are NOT the "closure at infinity"
The frequency does not change when dragging the cursor over here !

Zoomed, after plotting by the command nyquist at the prompt
Notes: n = 22

## Slide 4: TSPC_Exam_2015-11-06 extended Nyquist zoomed
Zoomed, after plotting by Sisotool

Notes: n = 22

## Slide 5: TSPC_Exam_2015-11-06 Bode diagrams
n = 22
The phase can/must be read “modulo 360° ”
180° discontinuity jump in phase at resonance frequency
Notes: n = 22

## Slide 6: TSPC_Exam_2015-11-06 root locus
 Actually plotted by Sisotool
stable loop
Notes: n = 22

## Slide 7: TSPC_Exam_2015-11-06 extended Nyquist with closure at infinity
>> nyquist1(Gp)
p =
-11.0000 + 0.0000i
0.0000 + 6.6332i
0.0000 - 6.6332i
Open loop poles
P =
0
P=number of Open loop poles in rhp
N =
1
N=number of clockwise encirclements
Z =
1
Z = P + N = number of closed loop poles in rhp
n = 22
Actually plotted by the script nyquist1.m



## Slide 8: TSPC_Exam_2015-11-06 extended Nyquist with closure at infinity
Zoomed, after plotting by nyquist1.m
add +1 to N
add −1 to N
default
zoomed directly on the figure


## Slide 9: TSPC_Exam_2015-11-06 extended Nyquist with closure at infinity
 Actually plotted by the script nyquistGUI.m
stable loop

## Slide 10: TSPC_Exam_2015-11-06 extended Nyquist with closure at infinity
Number of times that the extended polar plot of GOL(jω) encircles the (–1,0) point in the clockwise direction:
N = -1 +1 = 0
n = 22
Actually plotted by www.wolframalpha.com
