## Last name Tekeste Name Yeshitla Gebre student ID No.:0622800051
# Section 4: STABILITY OF LINEAR DYNAMIC SYSTEMS
A closed-loop dynamic system is made of P controller

Gc = Kc

a purely algebraic final control element with Gf = 1,
a process Gp having the following transfer function

a measuring device with

where n = 14

What is the open-loop feedback transfer function?

The open loop transfer function is =(1/14)/(s^2+196)^2*(s+14)

What is the open-loop system order?

The order of the open loop system is 5

Is the open-loop system an integrator process?

Yes it is an integrator process

Is the open-loop system a minimum phase system?
Yes it is! a minimum phase system. All poles lay to the LHP

How much is the open-loop system gain?

Kc= 1/(14)^6

How many and how much are the time constants?

There are two time constants which have the same values, T1=1/(14) and T2=1/(14)
Is there any damping factor? If there is, how much is  ?

the damping factor is  =0
## Part A: Root locus
For the open-loop dynamic system plot the root locus by means of Matlab and SisoTool resources, attach it here and answer the following questions:

he following graph shows the Plot of root locus by means of Matlab resources
The open loop transfer function for the system is given by =(1/14)/(s^2+196)^2*(s+14)

Determine poles, zeroes and No. of trajectories.

There are two complex poles each with multiplicity 2
0.0000 +14.0000i
   0.0000 -14.0000i
  -0.0000 +14.0000i
  -0.0000 -14.0000i

there is no zero
we have four trajectories

Do you use direct or inverse root locus rules? Why?

I used the direct root locus rule
Determine parts of root locus coincident with the real axis.

There is no part of the root locus that coincides with the real axis.
Discuss existence of asymptotes and, if possible, calculate the gravity center and angles formed with the real axis.

As K ® ¥ the loci approach asymptotes. There are q = n – m = 5asymptotes and they intersect the real axis at angles defined by (2k+1)/q = ere k=0,1,2,….,4
The asymptotes intersection point(gravity center) on the real is defined by
 a=(poles of GH(s)-zeros of GH(s))/q =

so we have q=5-0=5 and q-1=4

the angles they make with real axis are: 45, 135,225,315°,360°

Discuss and, if possible, calculate starting and ending angles for poles and zeroes.

Since we have two complex conjugate poles we have angle of departure but no angle of arrival since there is no complex zero.

ngle of Departure
p1  =  + [( p1-z1)+ ( p1-z2)+… +(- p1-zm)] – [( p1-p2)+( p1-p3)+….. +( - p1-pn)].
Angle of departure from pole at 14i

θdepart = 180° + sum(angle to zeros) - sum(angle to poles)=180+0-90=90°

for the conjugat the departure angle is -90°

Discuss and, if possible, calculate the breakaway points

When two or more loci meet on the real axis, they will break away from this point at particular angles. The point is known as a breakaway point. It corresponds to multiple roots. The angle of breakaway is 180°/k where k is the number of converging loci.
The location of the breakaway point is found from the solution of d(Gol)/ds=0
or can be calculated using or can be easily seen from the graph

there are two break away points each
each located at s= 0+15j, s=0-15j

Discuss the BIBO stability of the system when Kc is changed

the system is BIBO unstable for any controller gain

Calculate the limiting value/values for Kc, if any

there is no limiting values for kc it is unstable for all values

In the present case, is a switch from a P controller to a PD controller more favorable in view of closed-loop feedback stability? Why?

The PD controller achieves the desired set point quickly and stabilize the system compared to the P and PI controllers. Therefore, PD controller is best and preferable.

## Part B: Frequency response
For the open-loop dynamic system with Kc=1:

Plot the Bode Diagrams by means of Matlab/Sisotool resources and attach them here

Plot the asymptotic Bode Diagrams by means of ASBODE script and attach them here

Discuss the asymptotic behavior for low and high frequencies.

At low frequency the AR approaches -100 db, the argument (angle)approaches 0°
at high frequency AR approaches MINUS infinity in dB and the angle approaches 0°

Calculate AR for  = 20 rad/s
it is -115 db

Does a resonance frequency exist? How much is it?
Yes! there exist a resonance frequency, r= (1-2.2)1/2/=…… for =0…< 0.707. Resonance frequency occurs when < 0.707.
 r = 14

Does a crossover frequency exist? How much is it?

No there is not
Does a gain crossover frequency exist? How much is it?

Yes there is :wcg = 14.0095
In the asymptotic Bode plot AR is never 1

Check, on the base of the Bode stability criterion, if the above system is closed-loop stable

It is closed loop unstable……….. If at the phase crossover frequency, wcp  the corresponding log modulus of G(jwcp ) is less than 0 dB(1AR), then the closed-loop system is stable.

Because the gain is infinity greater than 1

Plot the Nyquist Diagram by means of Matlab/Sisotool resources and attach it here

Check, on the base of the Nyquist stability criterion, if the above system is closed-loop stable

It is closed loop stable………. If the open –loop Nyquist plot of a feedback system encircles the point (-1,0) as the frequency  takes value from - to +, the closed-loop response is unstable. It is stable otherwise. From the figure of nyquist at the frequency of point A the Nyquist plot intersects the unit circle around the origin. Therefore, since the distance of point A from the origin is the amplitude ratio at this frequency, we conclude that the angle between point A and the negative real axis represents the phase margin.

Calculate the gain margin and the phase margin, if any

GM= infinity

PM= 180°

1. What is the definition of ultimate gain Ku?
2. Calculate the ultimate gain Ku, if possible
## Part C: Dynamic responses in the time domain
For the open-loop dynamic system with Kc=1:

Plot the open-loop and closed-loop system dynamic responses to a unit step change in set point by means of Matlab resources, attach them here and give your comments.

The closed -loop system initially it was stable but after some settling time later it is unstable

the open loop step response initially small instability but later it becomes unstable through out.

Both open and closed loop step response are are unstable the given input

Plot the closed-loop system dynamic responses to a unit step change in disturbance du by means of Matlab resources, attach them here and give your comments.

Initially it is stable but finally it becomes sinusoidal not stable. It will notcome to stability.